## Slide 1
Auto-converted version of the PDF catalog as a PPT.
Some, but not all, of the content may be able to be
copied/pasted or isolated for use in other PPTs of your
own. Since this was auto-converted, please always
refer to the PDF file for any unclear formatting or values.

## Slide 2: WHAT’S NEXT? FLYING HORSES? UNICORNS? WHO KNOWS? ANYTHING IS POSSIBLE!
3
order@fulham.com
+1 323 599 5000
www.fulham.com
From the dawn of time, we humans have utilized creativity and inventiveness to manipulate our world through innovation. Imagining what is not yet but what could be, then making it so
has been a hallmark trait of some of the most noteworthy among us – those with an“Anything is Possible”mentality, even in the face of adversity, peer ridicule or doubt.
The imagination that advances our civilization applies to every facet of our lives, including lighting. From our
humblest beginnings – merely trying to lengthen our days with artificial light – to present day lighting technologies, we’ve been obsessed with controlling lighting. Our ability to do so has evolved through the dogged effort and ingenuity of generations of curious, brilliant humans.
Light is a physical phenomenon. Electromagnetic radiation. A universal raw material: photons, wavelengths, particles, optical receptors… but Lighting is the conscious manipulation of Light, developed over thousands of years. In these pages, we review the strides we’ve made in our field via the“giants”of our field who see no limits to what’s possible.
THE SUN, MOON & STARS
This was Square One. But life couldn’t come to a grinding halt just because the sun went down...
FIRE
Fire was good. It was humanity’s first stab at producing light on demand. Fire sparked our entry into controlled lighting. Over the ages, it led to candles, oil lamps and gas lighting. Although fire produced cheery light, it did have its dark side, like accidentally burning down the house. Still,
it was generally agreed that fire was… hot!
INCANDESCENT
The incandescent lamp (“light bulb”) came into widespread use roughly a century ago. Light is produced by a heated, glowing filament sealed in a gas-filled (or vacuum) tube. Electricity surges in; a filament heats up; the bulb glows, produces light.
HALOGEN
Halogen lamps are souped-up incandescent bulbs with a tungsten filament. The filament is engulfed in inert gas,
spiked with one of the halogen group of gases. When the tungsten heats up, its interaction with the gases triggers a chemical reaction.
During this halogen cycle, tungsten atoms stream from the bulb’s inside surface and back onto the tungsten filament. The lamp can run safely at higher
temperatures, can last longer, and has the added benefit of shining brighter per unit of electricity flowing through it.
HID
High Intensity Discharge (HID) lamps fall into the gas discharge lamp category. Their light output comes from electricity coursing between tungsten electrodes inside a tube filled with gas and metal salts.
Sparking the arc charges the salts into a “plasma” that glows intensely -- hence the word “intensity.” Despite their brilliance, HID lamps consume less energy than incandescent or fluorescent lamps, delivering more lumens per watt.
FLUORESCENT
Fluorescent lights are basically airtight tubes full of reactive gases that light up when electricity charges up their atoms, which then become... fluorescent. We even adapted this technology for specialty applications, such as UV germicidal purposes for purifying air and water, via modified lamps to kill germs. (See UV Germicidal Ballasts on page 50.)
Compact Fluorescent Lamps (CFLs) are often either pin-based
replacement lamps or self-ballasted, screw-based lamps that operate using fluorescent technology in various residential and commercial applications, due to their relatively small sizes and lesser energy draw
versus incandescent.
ELECTRODELESS TECHNOLOGIES
into light-emitting plasma. This technology delivers remarkable illumination from tiny lamps, but the cost of these ﬁxtures has made commercial adoption impractical.
LED
Light Emitting Diodes (LEDs) operate by electroluminescence – an optical phenomenon
in which electrical current triggers light emission as
it passes through semiconductor material. An LED light fixture is comprised of a fixture body, a diffuser lens, and an LED Light Engine. The LED Light Engine generally consists of an array of white (or color) LEDs placed on a printed circuit board (PCB) which is powered by an LED driver, an electronic component which precisely controls the flow
of electricity through the LEDs to ensure both quality of light and long life. LED Light Engines are generally tailored
to specific fixtures in order to meet e ciency, aesthetics, color consistency and life requirements.
WIRELESSLY CONNECTED LIGHTING CONTROL
Wireless Connectivity is to light what advanced music systems are to sound. Just as acoustic scientists created precise technologies to faithfully record,
fine tune, control and distribute music within sound environments, today’s lighting engineers have made equivalent advances in visual environments. Now one simple “smart” device can control a full range of lighting situations. You can program lighting to automatically manage a great variety of scenes, locally or remotely, by computer – even over the internet – from any place at any time with a handheld device.
Induction Plasma
Induction is essentially an offshoot of fluorescent technology but whose light-generating reaction uses an external electromagnetic field, rather than electrodes.
It lasts longer than standard fluorescent, but as the cost of LEDs fell, the utility of Induction severely diminished. Plasma was dubbed electrodeless HID. Plasma is created by heat or streamed electromagnetism. Radiating microwaves transform certain gases and other materials
LIGHTING FIXTURE POWER SUPPLY
3
2
2

## Slide 3: ON THE SHOULDERS OF GIANTS
5
4
According to the ancient parable he was citing, even a dwarf can see further than a giant if he stands on the giant’s shoulders. Sir Isaac -- indisputably an intellectual giant himself
-- modestly credited the “shoulders of giants” for his success. The expression acknowledges the contribution of earlier workers for one’s own achievements, since knowledge advances on the basis of previous knowledge.
But sometimes giants stand upon the shoulders of other giants. Consider the sequence of advances made by “giants” like Michael Faraday, James Maxwell, Nikola Tesla and Thomas Edison.
The solitary work of individual geniuses created a series of inspired lighting inventions. This
established the foundation for a universe of practical applications, developed by later generations of scientists and technicians. The lonely eccentric’s
makeshift workshop has given way to extravagantly equipped lab complexes staffed with teams of trained researchers. Nowadays it is common to see close collaboration among colleagues half a world apart; speaking different languages; people from vastly divergent cultural backgrounds
-- all working together in the common interest.
Technological and production advances will always be driven by inspired individual efforts. But in general, progress in our industry is the result
of solid teamwork. Nowhere is trans-national teamwork more evident than at Fulham. We are a worldwide company in manufacturing, marketing, sales and distribution. We also have world class R&D facilities in Asia, India and at our U.S. Headquarters, Our international research team includes some of the best brains in the industry from many diverse backgrounds.
All are united in Fulham’s dedication to exceeding customer expectations. This commitment has grown
us into a company that is truly trusted worldwide for cost
efﬁcient, innovative, reliable, relevant lighting solutions.
Thomas Edison
Charles Steinmetz
Elmer Fridich
Nikola Tesla
Peter Cooper Hewitt
If I have seen further than other men, it is because I have stood upon the shoulders of giants.
-- Sir Isaac Newton (1642 - 1727)
Jaap Haartsen
Michael Faraday
Shuji Nakamura
Nick Holonyak
Edward E. Hammer
4
5

## Slide 4
7
6
order@fulham.com
+1 323 599 5000
www.fulham.com
From our headquarters in Los Angeles and design centers in China and India, our teams of product managers and engineers work with our customers to conceive, design, manufacture and supply reliable, sustainable lighting solutions that bring cutting-edge, relevant innovation to a global market.
A Pioneer in Lighting Electronics
From its beginnings in 1994, Fulham has been dedicated to creative, sustainable lighting programs that give our users the power to build or install smart, differentiated, versatile lighting. Fulham’s revered product quality and world-class customer responsiveness make us the preferred partner to over 3,000 lighting manufacturers and distributors worldwide.
27
ThoroLED Programmable Constant Current LED Drivers
WorkHorse IP65 & IP66 Programmable LED Drivers 28 WorkHorse Specialty Grade Dimmable 29
Programmable IP66 CC Drivers SugarCube Constant Current Drivers EliteControl Programmable LED Driver ThoroLED Constant Voltage LED Drivers Lumo Series European LED Drivers
30
31
32
33
LIGHT SOURCES
Vizion 450mA ECO Series DC LED Modules
Vizion Cuttable LED Modules
Vizion Linear High Output DC LED Modules
36
36
37-38
Vizion Linear High Output LED Retrofit Kits
Vizion Outdoor Street, Wallpack & Canopy Modules
Vizion Highbay And Lowbay LED Modules
Vizion DirectAC LED Retrofit Kits
VividHorse 120V DirectAC LED Engines Retrofit Kits VividHorse DC LED Engine Retrofit Kits VividHorse Troffer & Panel LED Retrofits FarmHorse Horticultural Specialty LED Modules Vizion UVA & UVC Specialty LED Products
FLUORESCENT
IceHorse Low Temperature Ballasts SunHorse UV Germicidal & Tanning Ballasts WorkHorse Fluorescent Ballasts
50
50-51
52-53
EMERGENCY
HotSpot Plus LED Driver Emergency System 10 HotSpot Constant Power LED Emergency Drivers 11-13
HotSpot Constant Power LED Driver for AC Engines 13 FireHorse Emergency Power Supply/Micro-Inverter 14 FireHorse Fluorescent Emergency Ballasts 15
16-17
18-19
22-23
HotSpot2 LED Emergency System
HotSpot1 LED Emergency System
FireHorse Emergency Lights, EXITs & Running Man Signs
LED DRIVERS
PONY Selectable Current IP20 LED Drivers
26
LongHorse Remote Mount Ballasts
RaceHorse CFL & T5 Fluorescent Ballasts
PONY Electronic Ballasts
SugarCube Ballasts
43
44
45
46
47
53
54
54
55
58-59
CONTROLS
EliteControl SIG Qualified Bluetooth Mesh Lighting Control System
Why Choose Fulham? Warranty Information Contact Us
60
61
Back Cover
TABLE OF CONTENTS / TIMELINE
TABLE OF CONTENTS / TIMELINE

## Slide 5
8
order@fulham.com +1 323 599 5000 www.fulham.com 9
8
LED Emergency Lighting Solutions
Emergency Lighting has been an ESSENTIAL focus area for Fulham since the onset of the company, with its FireHorse branded products. Across time, Fulham’s “Anything is Possible” mentality has led to industry accolades for introduction of entirely new EM innovations – whether our HotSpot1 and HotSpot2 Systems, our Micro-inverters, our smallest form factor constant power 4W driver in the industry, our slim profile units, or Programmable EM Drivers for versatility and convenience.
Don’t see it? Ask for it, because Fulham’s Custom Capabilities are also ready to help make the impossible possible!
9

## Slide 6
11
10
order@fulham.com
+1 323 599 5000
www.fulham.com
HotSpot Plus LED Driver and Emergency System
Watts | Output Current (mA) | Output Voltage (VDC) | Model Number Input Voltage Dimming Ch. Dimensions Case Type (VAC) Type (L x W x H) |  |  |  |  | 
40 | 250-1400 | 11-55 | FHSAC1-UNV-40BLS* | 120-277; 50/60Hz | 0-10V | 1 | 6.37” x 3.13” x 1.54” | Compact w/ Bottom Leads
40 | 250-1400 | 11-55 | FHSAC1-UNV-40C* | 120-277; 50/60Hz | 0-10V | 1 | 6.32” x 3.13” x 1.14” | Compact w/ End Leads
40 | 250-1400 | 11-55 | FHSAC1-UNV-40L** | 120-277; 50/60Hz | 0-10V | 1 | 9.49” x 2.40” x 1.34” | Linear w/ End Leads
70 | 350-2400 | 11-55 | FHSAC1-UNV-70S*** | 120-277; 50/60Hz | 0-10V | 1 | 16.70” x 1.18” x 1.00” | Linear w/ Terminals
HotSpot Plus Accessories
FHS-TSTWL-BC IP67, bicolor LED Indicator / test switch for use in exposed, outdoor-rated luminaires for 40W models FHS-TSTWL-BC-S* IP67, bicolor LED Indicator / test switch for use in exposed, outdoor-rated luminaires for 70W model FHS-EXT-48-TST 48” test switch extension cable
*Made to Order
HotSpot Plus LED Driver & Emergency System
The revolutionary HotSpot Plus LED Driver & Emergency System combines the functions of a dimmable, programmable LED driver, emergency LED driver, and replaceable backup battery in a single compact unit. Under normal conditions this all-in-one solution operates as a constant current driver; during a power outage the integrated battery automatically activates, providing reliable emergency illumination for safe building egress. Benefits include smaller size, simplified installation, and the ability to bring emergency LED capability to smaller luminaires.
Programmable output current in 1mA increments
UL 924 Self-Diagnostics
Selectable emergency output:
40W models: 5W for 180 minutes or 10W for 90 minutes
70W model: 7W for 90 minutes, programmable for lower power and longer runtime
Compact size and simple installation for maximum flexibility
The Power of Programmability
All HotSpot LED drivers feature Fulham’s innovative SmartSet programming platform, which gives the user the power to create the right driver for any situation.
Auto-Programming capability for high volume usage
Driver does not need to be powered during programming
Programming via handheld controller or PC software
To see the Fulham SmartSet programming platform in action visit the links below: Overview of basic programming features: www.fulham.com/smartsetprogramming
One touch Auto-Programming: www.fulham.com/smartsetauto
Programming custom dimming curves: www.fulham.com/smartsetdimmingcurve
TPSB-100
SmartSet Controller
SmartSet Software
Specifications |  |  |  |  | 
Input Voltage | 120-277V (UNV) | Recharge Time | 24 Hours | Illumination Time | Minimum 90 minutes
Output Voltage | 10-55VDC | Ambient Temperature | 0ºC - 50ºC | RFI/EMI | FCC Part 15A Non-Consumer
Surge Protection | Per C62.41 (TVS) | Output Type | Class 2 |  | 
HotSpot Constant Power LED Emergency Drivers
Adds field-installable emergency capability to LED luminaires. Provides backup power to the luminaire’s LED modules for at least 90 minutes. The cULus Classified driver is designed for flexibility, with multiple mounting options, a conduit feed, and an illuminated test switch.
HotSpot Constant Power LED Emergency Drivers |  |  |  | 
Model Number (CEC Title 20) | Output Power (W) | Output Lumens* | Output Current (mA) | Dimensions (L x W x H)
FHSCP-UNV-5WL | 5 | 800 | 90-500 | 11.5” x 2.6” x 1.5”
FHSCP-UNV-7.8WL | 7.8 | 1250 | 140-780 | 15.4” x 2.6” x 1.5”
FHSCP-UNV-10.7WL | 10.7 | 1700 | 195-1007 | 15.4” x 2.6” x 1.5”
FHSCP-UNV-13.7WL† | 13.7 | 2200 | 250-1370 | 19.2” x 3.03” x 1.63”
FHSCP-UNV-17WL | 17 | 2700 | 300-1700 | 19.2” x 3.03” x 1.63”
* Based on 160 lumens/Watt light source
† Made to Order
eatures
s. Complete
include self-diagnostics and detailed data logging. Meets CEC Title 20 battery charger requirement system includes emergency driver and emergency battery.
Specifications |  |  | 
Model Number | FHSCP-UNV-10P-L-SD | Output Type | Class 2
Input Voltage | 100-277VAC, 50/60Hz | RFI/EMI | FCC Part 15A Non-Consumer
Input Current | 0.06A Max. | Ambient Operating Temperature Range | 10°C to 55°C (50°F to 131°F)
Output Power | 3-10W | Dimensions (L x W x H) | 7.91” x 2.05” x 1.17”
Output Current | 620mA Max. | Battery Type / Recharge Time | LiFePO4 9.6VDC / 12 Hours
Output Voltage Range | 16-55VDC | Input Surge Protection | Line-Neutral 2kV, Line & Neutral-Ground 2kV
Number of Output Channels | 1 | Warranty | 5 years
Self-Diagnostics | Factory-enabled by default, can be disabled by luminaire manufacturer |  | 
Bicolor LED Indicator | Included LED indicator/test switch provides automatic system status updates |  | 
s. Complete
FHSBATL3-3-SD* | 10W | 3000mAh | 9.6V | LiFePO4 | Compliant | 12 hours | 4.39” x 2.92” x 1.30”
FHSBATL6-1.5L-SD | 10W | 3000mAh |  |  |  |  | 9.13” x 1.63” x 0.97”
FHSBATT8-C3L-SD* | 10W | 3000mAh |  | NiCd | Exempt | 24 hours | 9.25” x 2.11” x 1.21”
HotSpot Constant Power Programmable Battery Packs
Model Number
Max. Load for 90 Min
Capacity
Battery Voltage
Battery Type
RoHS
Recharge Time
Dimensions (L x W x H)
FHSBATL3-1.5-SD*
5W
1500mAh
3.48” x 2.87” x 0.96”
FHSBATL9-.6-SD*
6W
1800mAh
7.52” x 1.87” x 0.79”
*Made to Order
*cURus **cULus, CE ***cULus
= Self-Diagnostic
EMERGENCY
EMERGENCY
LED EMERGENCY SYSTEMS
LED EMERGENCY SYSTEMS
HotSpot Constant Power Programmable LED Emergency Driver
Provides programmable, constant power emergency output for existing LED modules. Advanced f atures

## Slide 7
13
12
order@fulham.com
+1 323 599 5000
www.fulham.com
Specifications
Model Number | FHSCP-UNV-10P-S-SD | Output Type | Class 2
Input Voltage | 120-277VAC, 50/60Hz | RFI/EMI | FCC Part 15A Non-Consumer
Input Current | 0.1A Max. | Ambient Operating Temperature Range | 0°C to 55°C (32°F to 131°F)
Output Power | 3-10W | Dimensions (L x W x H) | 16.7” x 1.18” x 1.00”
Output Current | 666mA Max. | Battery Type / Recharge Time | Lithium 11.1VDC / 12 Hours
Output Voltage Range | 15-55VDC | Input Surge Protection | Line-Neutral 1kV, Line & Neutral-Ground 2kV
Number of Output Channels | 1 | Warranty | 5 years
Self-Diagnostics | Factory-enabled by default, can be disabled by luminaire manufacturer |  | 
Bicolor LED Indicator | Included LED indicator/test switch provides automatic system status updates |  | 
Specifications
Model Number | FHSCP-UNV-6W-L-SD | Output Type | Class 1
Input Voltage | 120-277VAC, 50/60Hz | RFI/EMI | FCC Part 15A
Input Current | 0.85A Max. | Ambient Operating Temperature Range | 0°C to 50°C (32°F to 122°F)
Output Power | 6W | Dimensions (L x W x H) | 9.5” x 2.4” x 1.49”
Normal Output Voltage Range | 120-277VAC | Battery Type / Recharge Time | Ternary Lithium Battery 11.1VDC / 12 Hours
Emergency Output Voltage Range | 60-230VDC | Input Surge Protection | Line-Neutral 1kV, Line & Neutral-Ground 2kV
Number of Output Channels | 1 | Warranty | 5 years
Self-Diagnostics | Factory-enabled by default, can be disabled in the field |  | 
Bicolor LED Indicator | Included LED Indicator/test switch provides automatic system status updates |  | 
CONSTANT POWER IN-FIXTURE EM
FHSCP-UNV-10P-S-SD
10 Watt Slim Emergency System Approximately 50% smaller than competition
FHSCP-UNV-6W-L-SD
Field-Installable 6 Watt Emergency Driver for AC Engines
Provides constant power emergency output for existing LED modules. Meets CEC Title 20 battery charger requirements. This system includes emergency driver and integrated battery.
Most cost-effective emergency solution designed to operate Fulham AC LED engines (Ex. linear, round, rectangular)
Provides programmable, constant power emergency output for existing LED modules. Advanced features include self-diagnostics and detailed data logging. Meets CEC Title 20 battery charger requirements. This system includes emergency driver and integrated battery.
Specifications
Model Number | FHSCP-UNV-4W-L | Output Type | Class 2
Input Voltage | 120-277VAC, 50/60Hz | RFI/EMI | FCC Part 15A Non-Consumer
Input Current | 0.1A Max. | Ambient Operating Temperature Range | 5°C to 55°C (41°F to 131°F)
Output Power | 4W | Dimensions (L x W x H) | 5.34” x 1.69” x 1.01”
Output Current | 333mA Max. | Battery Type / Recharge Time | LiFePO4 6.4VDC / 12 Hours
Output Voltage Range | 12-55VDC | Input Surge Protection | Line-Neutral 1kV, Line & Neutral-Ground 2kV
Number of Output Channels | 1 | Warranty | 5 years
EMERGENCY
EMERGENCY
LED EMERGENCY SYSTEMS
LED EMERGENCY SYSTEMS
The Lighting Industry’s Smallest 4 Watt Emergency Constant Power LED Driver
FHSCP-UNV-4W-L
FHSCP-UNV-12W-L-SD
= Self-Diagnostic
Coming Soon
CONSTANT POWER EMERGENCY LED DRIVER
120-277V~ (UNV), 50/60Hz
12-55VDC Output
Output Wattage: 12W
IP20
Battery Charge Time 90 Mins
LED Class 2 Output Class
Remote Mount Test Switch
Battery Over / Under Voltage Protection
Battery Hot Plug at Normal and Emergency Mode Protection
Output Open Protection
Output Short Protection
5 Year Warranty

## Slide 8
15
14
order@fulham.com
+1 323 599 5000
www.fulham.com
Wide range of lamp and ballast compatibility
CEC Title 20 Compliance Standard
UL listed for damp locations
Integrated LED power indicator/test switch
LAMP APPLICATIONS
FT18W
FT24W
2
FT27W
FT36W
1 or 2
FT39W
FT40W
1
FT50W
FH7 FH11 FH12
FT - 4 pin
1 2
1 1 or 2
1 1 or 2
1 1
1 1
1 1
1
FT55W 1 1
CFQ - 4 pin
CFQ13W 1 2
CFQ18W 1 2
LAMP APPLICATIONS
FH12
FH7 FH11
2D - 4 pin
2D21W 1
2D28W 1 1 or 2 1 or 2
2D - 4 pin
2D38W 1 1 or 2 1 or 2
T5-Standard
F14T5 1 1 2
F21T5 1 1 1
F28T5 1 1 1
F35T5 1 1
T5-HO High Output
F24T5HO 1 1 2
LAMP APPLICATIONS
FH7 FH11 FH12
T8- Standard (continued)
F58T8
1
1
F70T8
1
1
T8-HO High Output
F60T8HO 1 1
F72T8HO 1 1
T8-SL Slim Line
F96T8SL 1
T12-Standard
F20T12 1 2 2
F30T12 2 2
FB34T12 1 or 2
CFQ26W | 1 | 1 | 2 |  | F39T5HO | 1 | 1 | 1 or 2 |  | F40T12 | 1 or 2 | 2
 | CFTR - 4 pin |  |  |  | F49T5HO |  |  | 1 |  | F40T12 ES (34W) | 1 or 2 | 
CFTR13W | 1 | 2 |  |  | F54T5HO (49W) | 1 | 1 |  |  | F75T12, F85T12 | 1 | 
CFTR18W | 1 | 2 |  |  | F54T5HO | 1 | 1 | 1 |  | F85T12 | 1 | 
CFTR26W 1 2 T8- Standard T12-HO High Output CFTR32W 1 1 2 F17T8 1 2 2 F48T12HO 1 CFTR42W 1 1 F25T8 1 1 or 2 2 F60T12HO 1 1 Circular-FCRT5 FB29T8 1 F72T12HO 1 22WCRT5 1 1 FBO31T8 1 F96T12HO (95W) 1 40WCRT5 1 1 F32T8 (25W) 1 1 F96T12HO (110W) 1 1 |  |  |  |  |  |  |  |  |  |  |  | 
150W Install (Six 25W Luminaires) 25W EM power distributed across install | 55WCRT5 | 1 | F32T8 (28W) | 1 | 1 | 2 | T12-SL Slim Line
(4.16W EM power per luminaire) Circular-FCRT9 F32T8 (30W) 1 1 F60T12SL 1 32WCRT9 1 1 F32T8 (32W) 1 1 1 or 2 F96T12SL 1 1 40WCRT9 1 1 F40T8 1 1 1 |  |  |  |  |  |  | 
FireHorse Lamp Operation | Also works with TLEDs. Check lamp manufacturers’ specifications for compatibility.
Specifications |  | 
Operating Voltage | 120-277V (UNV) | Fixture Wiring Switched or Unswitched Minimum Emergency Operation 90 Mins.
Frequency | 50/60Hz | Min. Required Charging Time 24 Hours
Regulatory Compliance | Meets or Exceeds N.E.C./LSC | Test Switch / Indicator LED Push Button
Battery Type | High Temp. Long Life Rechargeable NiCd | Optional Wall Plate: FHSWLPWH Used for remote mounting of test switch
FireHorse Ballast Models |  |  |  |  |  |  | 
Model Number | AC Standby Input Power (W) Rating (W) | Max Charge Current | Battery Voltage (VDC) | Battery Rating (Wh) | Dimensions (L x W x H) | Weight (lbs) | Warranty (Yrs.)
FH7-UNV-500L-CEC | 3 | 0.7 | 120VAC: 40 mA | 277VAC: 30mA | 6.0 | 12.0 | 9.60” x 2.16” x 1.13” | 1.7 | 
FH11-UNV-750L-CEC | 4 | 0.4 | 120VAC: 53mA | 277VAC: 30mA | 3.6 | 14.4 | 9.37” x 2.33” x 1.53” | 2.0 | 
FH11-UNV-750L-CEC-A† | 4 | 0.4 | 120VAC: 53mA | 277VAC: 30mA | 3.6 | 14.4 | 9.37” x 2.33” x 1.53” | 2.0 | 5
FH12-UNV-1400L-CEC | 4 | 0.7 | 120VAC: 60mA | 277VAC: 40mA | 12.0 | 24.0 | 14.58” x 2.17” x 1.23” | 1.7 | 
† Conduit feed
Fluorescent Emergency Ballasts
25W Micro-Inverter / Emergency Power Supply
Expected by Q1 2024: 50W Inverter FHUPS1-UNV-50-L-SD, 120/220/277 VAC Output, 320W Fixture max, 0-10V Dimming
Fulham’s innovative, new Micro-Inverter offers the ability to power any fixture in emergency mode at 25W for a period of 90 minutes.
Its uniqueness stems from its ability to run a fixture GREATER than 25W by using built-in 0-10V dimming wires. For example, the unit will scale down the power of a 150W fixture to 25W in Emergency Mode, allowing customers to use this inverter in high output applications where previously a costly inverter was the only solution.
The FHUPS1-UNV-25L-SD can support one fixture rated for 150W or multiple fixtures whose system wattage adds up to 150W in normal operation (although anything greater exceeds the input power rating of the unit.) This reduces the number of SKUs needed for emergency fixtures to save money.
Works with any 0-10V fixture(s) ≤150W for 25W of Constant Emergency Power for 90 minutes
Uninterrupted Power Supply
UL listed and CEC Title 20 compliant
Dims luminaires of up to 150W down to 25W(45VA) in emergency with 0-10V dimming; 25W(45VA) max without 0-10V dimming
Conduit for leads
Under voltage protection, short circuit protection, overload protection
Easy installation time: no need to open up a luminaire to connect this device to the driver.
Can be used with luminaires where the driver is not accessible,
e.g. UFO high bays
Saves money: higher wattage fixtures previously required a higher wattage/higher cost inverter
Self diagnostic standard
RJ11 port allows Bluetooth compatibility
Wiring one single luminaire without 0-10V dimming
Wiring multiple luminaires without 0-10V dimming
Specifications
Model Number | FHUPS1-UNV-25L-SD | Output Type | Class 1
Input Voltage | 100-277VAC, 50/60Hz | RFI/EMI | FCC Part 15A
Input Current | 0.12A Max. | Ambient Operating Temperature Range | 0°C to 50°C (32°F to 122°F)
Input Power | 11W | AC Drive Input Power | 150W Max (0-10V dimming required past 25W)
Output Power | 25W (45VA) Max | Dimensions (L x W x H) | 15.3” x 2.9” x 1.5”
Normal Output Voltage Range | 120-277VAC | Battery Type / Recharge Time | LiFoPo4 3600mAh / 12 Hours
Emergency Output Voltage Range | 120/220/277VAC | Input Surge Protection | Line-Neutral 1kV, Line & Neutral-Ground 2kV
Number of Output Channels | 1 | Warranty | 5 years
Self-Diagnostics | Factory-enabled by default, can be disabled in the field |  | 
Bicolor LED Indicator | Included LED Indicator/test switch provides automatic system status updates |  | 
One 25W luminaire powered at 100% during emergency
AC Out
25W
Five 5W luminaires powered at 5W each during emergency
AC Out
5W
5W
5W
5W
5W
25W
25W
25W
= Self-Diagnostic
Wiring multiple luminaires with 0-10V dimming
AC Out 0-10V Dimming Out
25W 25W 25W
MICRO-INVERTER & FLUORESCENT EMERGENCY BALLASTS
MICRO-INVERTER & FLUORESCENT EMERGENCY BALLASTS
EMERGENCY
EMERGENCY

## Slide 9
17
16
complete system is composed of an emergency driv
emergency battery, and output wire harness. A wide
The HotSpot2 emergency lighting system drives existing constant current LED modules during power outages. A complete system is composed of an emergency driver,
emergency battery, and output wire harness. A wide range of lumen output and run times are available.
HotSpot2 Drivers
FHSBATL3-1 | 3.48” x 2.35” x 0.99” | LiFePO4 | 1000 | 3 Cells | 24Hrs | 4 | 4
FHSBATL6-.6 | 5.23” x 1.87” x 0.85” | LiFePO4 | 1200 | 6 Cells | 24Hrs | 6 | 4
FHSBATL3-1.5 | 3.48” x 2.76” x 0.99” | LiFePO4 | 1500 | 3 Cells | 24Hrs | 8 | 8
FHSBATL3-1.5S | 8.87” x 1.11” x 0.96” | LiFePO4 | 1500 | 3 Cells | 24Hrs | 8 | 8
FHSBATL9-.6 | 7.52” x 1.87” x 0.85” | LiFePO4 | 1800 | 9 Cells | 24Hrs | 10 | 8
FHSBATCC3-3† | 6.00” x 3.60” x 1.55” | LiFePO4 | 3000 | 3 Cells | 24Hrs | 14* | 14*
FHSBATL6-1.5 | 5.70” x 2.76” x 0.99” | LiFePO4 | 3000 | 6 Cells | 24Hrs | 16 | 14
FHSBATL6-1.5L (with optional mounting bracket) FHSBATL6-1.5S | 7.89” x 1.56” x 0.92” 9.07” x 1.63” x 0.93” 16.67” x 1.11” x 0.96” | LiFePO4 LiFePO4 | 3000 6 Cells 24Hrs 16 14 3000 6 Cells 24Hrs 16 14 |  |  |  | 
FHSBATT8-C3 | 4.15” x 3.29” x 2.11” | NiCd | 3000 | 8 Cells | 24Hrs | 16 | 16
FHSBATT8-C3L (with optional mounting bracket) | 7.89” x 2.17” x 1.04” 9.07” x 2.18” x 1.07” | NiCd | 3000 | 8 Cells | 24Hrs | 16 | 16
FHSBATL3-3 | 4.39” x 2.82” x 1.3” | LiFePO4 | 3000 | 3 Cells | 24Hrs | 16 | 16
FHSBATT8-D4*** | 4.89” x 3.84” x 2.72” | NiCd | 4000 | 8 Cells | 24Hrs | 20 | 20
FHSBATL6-3 | 7.52” x 2.82” x 1.3” | LiFePO4 | 6000 | 6 Cells | 32Hrs | 20** | 20**
FHSBATL6-3L (with optional mounting bracket) | 7.94” x 2.17” x 1.21” 9.13” x 2.21” x 1.28” | LiFePO4 | 6000 | 6 Cells | 32Hrs | 20** | 20**
FHSBATCC3-3-40C†† | 6.00” x 3.87” x 1.87” | LiFePO4 | 3600 | 3 Cells | 24Hrs | 20 | 20
† Cold Pack Battery: -20°C minimum operating temperature * Rated 10W for Canada ** Rated 16W for Canada *** Made to Order † † -20°C =20W, -30°C =10W, -40°C =6W rating
 | Model Number | mA | Model Number | mA | Model Number | mA
Wiring harnesses: | FHS-HARNESS-100 | 100 | FHS-HARNESS-250 | 250 | FHS-HARNESS-550 | 550
Used to set the output current to | FHS-HARNESS-125 | 125 | FHS-HARNESS-300 | 300 | FHS-HARNESS-600 | 600
the LED module during emergency | FHS-HARNESS-150 | 150 | FHS-HARNESS-350 | 350 | FHS-HARNESS-650 | 650
operation. Using lower current will allow longer | FHS-HARNESS-175 | 175 | FHS-HARNESS-400 | 400 | FHS-HARNESS-700 | 700
run times. | FHS-HARNESS-200 | 200 | FHS-HARNESS-450 | 450 |  | 
 | FHS-HARNESS-225 | 225 | FHS-HARNESS-500 | 500 |  | 
FHS-EXT12M | 12” battery extension cable |  |  |  |  | 
FHS-EXT-48-TST | 48” test switch extension cable |  |  |  |  | 
Also available: battery mounting brackets and wallplates. For more information, visit www.fulham.com
order@fulham.com +1 323 599 5000 www.fulham.com
HotSpot2 Accessories
FHS-TSTWL
IP67, test switch for use in exposed, outdoor-rated luminaires
FHS-TSTWL-BC
IP67, bicolor LED Indicator / test switch for use in exposed, outdoor-rated luminaires
HotSpot2 LED Emergency System
Model Number (CEC Title 20) | FHS2-UNV-36L FHS2-UNV-56S
Input Voltage | 100-277VAC
Input Frequency | 50/60Hz
Input Current | 0.1A Max
LED Currents | 100mA - 700mA
Standby Input Power | <0.8W
Total LED Power | 20W
Input Surge Protection | 2.5KV Ring Wave
Over Current Protection | Fuse
Illumination Time | 90 - 350 Min
LED Connection | Series
LED Output Protection | Self Resetting PTC
Output Classification | UL1310/Class 2
Bicolor LED Indicator | Included LED indicator / test switch provides auto- matic system status updates
Output Voltage | 12 - 55VDC 12 - 56VDC
Dimension (L x W x H) | 5.34” x 1.69” x .93” 9.5” x 1.18” x 1”
ot2 Emergency Battery Packs
HotSpot2 Emergency Battery Packs
HotSpot2 LED Emergency System
HotSpot2 in Operation During Power Outage
Unlike the HotSpot1 LED Emergency System that comes equipped with separate LED modules, the HotSpot2 system operates a fixture’s existing LED modules in emergency mode. HotSpot2 is a CEC-compliant, UL924 recognized emergency lighting system for use with LED modules driven by a constant current source.
The battery charger automatically adjusts to the connected battery, and output current can be set by a wiring harness or Fulham’s SmartSet programming software, allowing a wide range of lumen outputs and runtimes. Self-diagnostic capability reduces liability and maintenance costs.
LED Fixture in Normal Operation
EMERGENCY
EMERGENCY
LED EMERGENCY SYSTEMS
LED EMERGENCY SYSTEMS

## Slide 10
19
18
order@fulham.com
+1 323 599 5000
www.fulham.com
HotSpot1 systems add LED emergency lighting capability to existing luminaires, including TLED luminaires and retrofit projects. UL Classified kits are approved for field installation and are ideal for both fluorescent and Type A and B LED tubes. A complete kit includes an emergency driver, module, battery, installation instructions, and all necessary hardware and labels. The system operates independently of the luminaire’s light source, ensuring compatibility with many types of luminaires.
Seamlessly add inconspicuous emergency lighting capability to existing non-emergency fixtures, such as recessed lighting and wall sconces, with the HotSpot1 modular LED systems.
A wide choice of lumen output levels, run times, discrete size, universal input voltage, and plug-n-play low voltage output wiring provide extreme adaptability, low cost of installation, and a high level of safety during operation.
HotSpot1 LED Emergency Retroﬁt Kits
W
rks with Type A and Ty
pe B TLEDs
Output
Model Number Watts Lumen |  |  | Comparable Fluorescent Lumen Output | Estimated Run Time (Mins) | Module Dimensions (L x W) | Case Qty.
Linear Module |  |  |  |  |  | 
FHSKITT03LNC† | 3 | 450 | 720 | 145 | 4.68” x 0.82” | 10
FHSKITT03LND† | 3 | 450 | 720 | 200 | 4.68” x 0.82” | 10
FHSKITT03LNF† | 3 | 450 | 720 | 360 | 4.68” x 0.82” | 20
FHSKITT03LNFL*† | 3 | 450 | 720 | 360 | 4.68” x 0.82” | 20
FHSKITT04LNC | 4 | 500 | 800 | 145 | 4.68” x 0.82” | 10
FHSKITT04LND | 4 | 500 | 800 | 200 | 4.68” x 0.82” | 10
FHSKITT04LNF | 4 | 500 | 800 | 360 | 4.68” x 0.82” | 20
 |  |  | Linked Linear (2 Mod | ules) |  | 
FHSKITT07LND† | 7 | 900 | 1440 | 100 | 4.68” x 0.82” | 10
FHSKITT07LNF† | 7 | 900 | 1440 | 180 | 4.68” x 0.82” | 20
FHSKITT07LNFL*† | 7 | 900 | 1440 | 180 | 4.68” x 0.82” | 20
 |  |  | Linked Linear (3 Mod | ules) |  | 
FHSKITT10LNF | 10 | 1350 | 2160 | 120 | 4.68” x 0.82” | 20
FHSKITT10LNFL* | 10 | 1350 | 2160 | 120 | 4.68” x 0.82” | 20
 |  |  | Small-H Module |  |  | 
FHSKITT06SHC | 6 | 750 | 1200 | 90 | 3.54” x 3.93” | 10
FHSKITT06SHD | 6 | 750 | 1200 | 125 3.54” x 3.93” 10 |  | 
FHSKITT06SHF | 6 | 750 | 1200 | 235 | o 3.54” x 3.93” | 20
FHSKITT10SHF | 10 | 1250 | 2000 | 135 | 3.54” x 3.93” | 20
 |  |  | Large-H Module |  |  | 
FHSKITT08LHD | 8 | 1000 | 1600 | 90 | 5.71” x 3.93” | 10
FHSKITT08LHF | 8 | 1000 | 1600 | 175 | 5.71” x 3.93” | 20
FHSKITT10LHF | 10 | 1250 | 2000 | 135 | 5.71” x 3.93” | 20
* Linear battery
† 3W and 7W kits are UL Marine Classified
HotSpot1 Emergency Driver | 
Model Number | FHS1-UNV-3.6L
Input Voltage | 100-277VAC (UNV)
Input Frequency | 50/60Hz
Input Current | 0.06 A Max.
Input Wattage | 10W Max.
Standby Input Power | <0.8W
Compatible Batteries | NiCd, 3.6 VDC
Battery Capacities | 3AH, 4AH, 8AH
Total LED Power | 1-10W
Illumination Time | 90 - 360 Min.
Surge Protection | C62.41 (TVS)
Over Current Protection | Fuse
Recharge Time | 32 - 48 Hrs
LED Connection | Parallel
LED Output Protection | Self Resetting PTC
Output Classification | UL1310/Class 2
HotSpot1 Emergency Battery Packs |  |  |  | 
Model Number | Battery Qty/Type | Operation Duration | Output Power/Time | Dimensions (L x W x H)
FHSBATT3-C3 | 3/C | 3 Amp/Hrs | 4W: 145min, 6W: 90min | 3.1” x 2.00” x 1.00”
FHSBATT3-D4 | 3/D | 4 Amp/Hrs | 4W: 200min, 6W: 125min, 8W: 90min | 4.00” x 2.50” x 1.35”
FHSBATT3-F7 3/F
8 Amp/Hrs
4W: 360min, 6W: 235min, 8W: 175min, 10W: 135min
4W: 360min, 6W: 235min,
4.00” x 3.60” x 1.35”
FHSBATT3-F7L 3/F
8 Amp/Hrs
8W: 175min, 10W: 135min
11.75” x 1.56” x 1.37”
HotSpot1 Emergency Modules |  |  | 
Model Number | Watts | Shape | Applications
FHS6-AR-3WL | 3 | Linear | Wall sconce, ceiling flush mount, low level lighting
FHS1-AR4-WL | 4 | Linear | Wall sconce, ceiling flush mount, low level lighting
FHS3-AR-6W-SH | 6 | Small-H | Wall sconce, ceiling flush mount
FHS4-AR-8W-LH | 8 | Large-H | Wall sconce, ceiling flush mount
FHS3-AR-10W-SH | 10 | Small-H | Wall sconce, ceiling flush mount
FHS4-AR-10W-LH | 10 | Large-H | Wall sconce, ceiling flush mount
HotSpot1 LED Emergency System
HotSpot1 LED Emergency System
Linear
H-conﬁguration
HOTSPOT
HOTSPOT
LED EMERGENCY SYSTEMS & RETROFIT KITS
LED EMERGENCY SYSTEMS & RETROFIT KITS
EMERGENCY
EMERGENCY

## Slide 11
20
order@fulham.com +1 323 599 5000 www.fulham.com 21
20
EXIT Signs & Emergency Fixtures
Fulham’s suite of EXIT Signs, Running Man Signage and Emergency fixtures has been developed to cover all common applications (including some regional requirements, such as NYC EXITS), while also enhancing convenience with features such as self-diagnostic or remote capability. Looking for wet location, cold temp, impact resistant or high lumen output options? Look no further!
21

## Slide 12
23
22
order@fulham.com
+1 323 599 5000
www.fulham.com
Reliable, energy-e cient emergency lights in a variety of styles and sizes
Operation Mode
Features
Battery Back Up
Adjustable Heads
High Lumen Output
Low Profile Emergency Lighting
Model Number Housing Color Light Source
FHEM10W*†
FHEM10WH*† White LED
FHEM10WHU
High Lumen Output / Universal Voltage
FHEM12W†
Battery Back Up
Fully Adjustable Heads
FHEM12WW†
Fully Adjustable Heads / Wet Location
FHEM16W* ††
Battery Back Up
High Lumen Output / Remote Capability Available
FHEM17
Battery Back Up
800 Lumens / Fully-adjustable Square Heads / Impact Resistant / Dual Voltage 120V/277V / 90 min EM operation / Damp Location
White LED
White LED
White LED
White LED
FHEM18W*
Battery Back Up
600 Lumens / Thin with Round Adjustable Heads / Remote Capable Option / Self- Diagnostic Option
* CEC Title 20 Compliant
†
These models are UL Listed, not cULus.
†† The FHEM16W is not available with Self-Diagnostic
Emergency Lighting / Exit Sign Combo
Model Number Description Housing Color Letter Color
Operation Mode
Features
Combo White
FHEC30WR Red
Battery Back Up
Micro LED Heads
FHEC30WG Green
FHEC33WR Red
High Brightness Combo White
FHEC33WG Green
FHEC34R* Red
Wet Location Combo White
FHEC34G* Green
Battery Back Up
LED High Output Heads /
Remote Capability Available
LED High Output Heads
Battery Back Up
Red Only: Cold Weather Heater for use down to -20°C
Wet Location / Remote Capability Available
Thermoplastic Slim Adjustable Combo
White
FHEC35R Red
Battery Back Up
Self-Diagnostics and Remote Capability Available
FHEC35G Green
*These models are UL Listed, not cULus.
= Self-Diagnostic
Emergency Lighting / Exit Sign Combo
Versatile emergency light and exit sign combination units with remote head capability
Emergency Lighting
Model Number Description Housing Color Letter Color Operation Mode Features
Slim Profile Thermoplastic Micro LED Exit Sign
FHEX20WREM** Red
White Battery Back Up Micro LED
FHEX20WGEM** Green
FHEX21WREM Red
Thin Profile Thermoplastic LED Exit Sign
White
Battery Back Up
Self Diagnostic Capability Available
FHEX21WGEM Green
FHEX21WRAC Red
AC Only
FHEX21WGAC Green
FHEX23ASGEM Edge-Lit LED Exit Sign Aluminum Green
Battery Back Up
Recessed Mount
Edge-Lit LED Exit Sign Aluminum
FHEX24ASREM* Red
Battery Back Up
Surface Mount
FHEX24ASGEM* Green
Battery Back Up
Cold Weather Heater available for use down to -20°C
FHEX26R Red
Wet Location LED Exit Sign White
FHEX26G Green
Wet Location / Remote Capability Available
* Refer to Spec Sheet for active part numbers.
** This model is cULus Listed.
Dependable LED exit signs with slim profile and edge-lit options
LED Exit Signs
We also offer Regional Emergency Exit items available for review online such as:
New York City Approved Exit Lighting
FHNY11
New York City Approved Exit Signage
FHNY31
Running Man LED Exit Sign
Single or double face with changeable legends. Comes standard with three pictogram legends for directional selection. cULus Listed, Damp Location Rated. 120VAC / 347VAC Input, Input Power 4W. High quality NiCad battery. Low power consumption and LED light source for reduced operation and maintenance costs. 75,000 hr life. High impact UV flame rated thermoplastic. Universal Mounting: Ceiling, wall or side mount.
HOTSPOT
HOTSPOT
EXIT EMERGENCY PRODUCTS
EXIT EMERGENCY PRODUCTS
EMERGENCY
EMERGENCY
FHEU20
= Self-Diagnostic
= Self-Diagnostic

## Slide 13
24
order@fulham.com +1 323 599 5000 www.fulham.com 25
25
24
LED Drivers
Frequent LED Driver line extensions, improvements and new product launches are a predictable trait, as we march ahead with growing numbers or Programmable and/or Current Selectable indoor and outdoor drivers of many form factors for nearly all applications. Fulham serves an international clientele requiring the highest quality and reliability standards for Constant Current and Constant Voltage drivers. Trust us to do the same for you, and let the Fulham Custom Shop work to your advantage, if you don’t see what you need.

## Slide 14
27
26
order@fulham.com
+1 323 599 5000
www.fulham.com
CONSTANT CURRENT LED DRIVERS
PROGRAMMABLE LED DRIVERS
DRIVERS
DRIVERS
Max Output Programable Typical Customizable Dimensions (inches) Part Number Form Output Input Voltage Output 0-10V Dimming Efficiency AUX Output Dimming Factor Power Voltage Range Current Range Range at Max Curves/Step L W H (VDC) (mA) Load Dimming |  |  |  |  |  |  |  |  |  | 
THCC-1M1UNV105P-30E | Linear | 30W | 120-277VAC 12~55VDC 350-1050mA | 100-1%, Dim to off | 85% | 12VDC/200mA | N/A | 11.02” | 1.14” | 1.02”
T1M1UNV105P-40E | Linear | 40W | 120-277VAC 10~57VDC 250-1050mA | 100-0% | 85% | N/A | YES | 10.83” | 1.22” | 0.98”
THCC-1M1UNV140P-50E | Linear | 50W | 120-277VAC 12~55VDC 400-1400mA | 100-1%, Dim to off | 86% | 12VDC/200mA | N/A | 11.02” | 1.14” | 1.02”
T1M1UNV105P-60E | Linear | 60W | 120-277VAC 10~57VDC 250-1050mA | 100-0% | 88% | N/A | YES | 9.33” | 1.59” | 1.18”
T1M1UNV105P-60F | Compact | 60W | 120-277VAC 10~57VDC 250-1050mA | 100-0% | 88% | N/A | YES | 4.98” | 2.99” | 1.22”
THCC-1M1UNV240P-85E* | Linear | 85W | 120-277VAC 10~55VDC 700-2400mA | 100-1%, Dim to off | 86% | 12VDC/200mA | N/A | 16.73” | 1.14” | 1.02”
*Coming Soon |  |  |  |  |  |  |  |  |  | 
PONY Selectable Current IP20 LED Drivers
PONY Selectable Current IP20 LED Drivers |  |  |  |  |  |  |  |  | 
Part Number | Max Output Power | Input Voltage | Output Voltage Range (VDC) | Selectable Current Range (mA) | 0-10V Dimming Range | Typical Efficiency at Max Load | Dimensions (inches) |  | 
 |  |  |  |  |  |  | L | W | H
PYCC-1M1UNV040S-20L | 20W | 120-277VAC | 30~42Vdc | 300 / 350 / 400 | 100-10% | 86% | 11.02” | 1.18” | 0.83”
PYCC-1M1UNV055S-30L | 30W | 120-277VAC | 30~42Vdc | 450 / 500 / 550 | 100-10% | 86% | 11.02” | 1.18” | 0.83”
PYCC-1M1UNV070S-30L | 30W | 120-277VAC | 30~42Vdc | 600 / 650 / 700 | 100-10% | 86% | 11.02” | 1.18” | 0.83”
PYCC-1M1UNV085S-40L | 40W | 120-277VAC | 30~42Vdc | 750 / 800 / 850 | 100-10% | 86% | 11.02” | 1.18” | 0.83”
PYCC-1M1UNV100S-40L | 40W | 120-277VAC | 30~40Vdc | 900 / 950 / 1000 | 100-10% | 86% | 11.02” | 1.18” | 0.83”
PYCC-1M1UNV115S-50L | 50W | 120-277VAC | 30~42Vdc | 1050 / 1100 / 1150 | 100-10% | 86% | 11.02” | 1.18” | 0.83”
PYCC-1M1UNV130S-60L | 60W | 120-277VAC | 30~42Vdc | 1200 / 1250 / 1300 | 100-10% | 86% | 11.02” | 1.18” | 0.83”
Part Numbering Key
P Y C C - 1 M 1 U N V 0 4 0 S - 2 0 E - A F C
With connectors (E), Leads (L) With Auxiliary power/dim to off (A) With Flicker Free, <4% (F)
CCT Selectable (C)
Made to order options: MOQ of 500pcs (special lead time applies)
Versatility and Convenience of Selectable Current with 3 preset currents per model (50mA intervals)
Mitigates Supply Shortages for dedicated items that are hard to find
Applications: Indoor - O ce
Class 2 output
cULus listed, Class P
0-10V dimmable from 100%-10%
Linear form factor with wires
IP20 rating
EMI: FCC Part 15 Class A
Input Surge Protection: Line-Neutral 1kV, Line & Neutral-Ground 2kV, RingWave 2.5kV
Ambient Temperature: -25°C - 50°C
The Power of Programmability
Fulham’s LED drivers feature our innovative
SmartSet programming platform, which gives the user the power to create the right driver for any situation.
Auto-Programming capability for high volume usage
Driver does not need to be powered during programming
Programming via handheld controller or PC software
To see the Fulham SmartSet programming platform in action visit the links below: Overview of basic programming features: www.fulham.com/smartsetprogramming
One touch Auto-Programming: www.fulham.com/smartsetauto
Programming custom dimming curves: www.fulham.com/smartsetdimmingcurve
TPSB-100
SmartSet Controller
SmartSet Software
Programmable Constant Current LED Drivers
Versatile, Convenient Programmable Drivers
Mitigates Supply Shortages for dedicated items that are hard to find
Universal Input 120-277VAC, Class 2 output
cULus listed, Class P or cURus
0-10V dimmable from 100%-1%, dim-to-off or 100%-0%
Form factors: Linear/Compact with Connectors
IP20 rating
Options with Auxiliary output
Handheld programmer or SmartSet software (TPSB-100)

## Slide 15
29
28
order@fulham.com
+1 323 599 5000
www.fulham.com
PROGRAMMABLE LED DRIVERS
PROGRAMMABLE LED DRIVERS
DRIVERS
DRIVERS
Versatile Programmable Outdoor Drivers
Class 2 output
0-10V Dimmable
Wire Type
EMI: FCC Part 15 Class B
Input Surge Protection: Line-Neutral 6KV, Line & Neutral-Ground 10KV
Aluminum Extrusion heatsink housing
Type HL
IP65 or IP66
SmartSet and Handheld Programmer: TPSB-100
LED Programmable Drivers (IP65 and IP66)
Part Number | Max Output Power | Input Voltage | Input Surge | Output Programable Voltage Output 0-10V Range Current Range Dimming (mA) | Certification | IP Rating | Efficiency @ Max Load 277VAC | Dimensions (inches)
 |  |  |  |  |  |  |  | L W H
T1M1UNV210P-60L*
Line-Neutral 4kV, 60W 120-277VAC Line & Neutral-
Ground 6kV
10-57VDC 500-2100mA 100-1%, Dim cULus Listed,
to Off Class P
isted,
Class P
isted, P
isted, P
 | Max Output | Output Voltage Range | Programable Output | Efficiency @Max Load |  | Dimensions (inches) | 
Part Number | Power | (VDC) | Current Range (mA) |  |  |  | 
 |  |  |  | @277VAC | L | W | H
IP65 | 89% | 9.49” | 1.69” | 1.14” |  |  |  |  |  |  |  | 
IP66 | 91.5% | 5.71” | 2.6” | 1.44” |  |  |  |  |  |  |  | 
IP65 | 88% | 6.69” | 2.56” | 1.26” | WHSG-1M1UNV105P-75L | 75W | 53-107 | 350-1050 | 92.30% | 5.71” | 2.6” | 1.44”
 |  |  |  |  | WHSG-1M1UNV140P-100L | 96W | 53-107 | 350-1400 | 92.30% | 5.71” | 2.6” | 1.44”
IP66 | 91.5% | 5.71” | 2.6” | 1.44” | WHSG-1M1UNV069P-100L | 96W | 96-102 | 500-690 | 92.30% | 5.71” | 2.6” | 1.44”
 |  |  |  |  | WHSG-1M1UNV420P-150L | 150W | 28-56 | 700-4200 | 91.50% | 6.5” | 2.6” | 1.44”
 |  |  |  |  | WHSG-1M1UNV208P-150L | 150W | 56-107 | 500-2080 | 91.50% | 6.5” | 2.6” | 1.44”
 |  |  |  |  | WHSG-1M1UNV100P-150L | 150W | 107-214 | 350-1000 | 91.50% | 6.5” | 2.6” | 1.44”
 |  |  |  |  | WHSG-1M1UNV560P-200L | 200W | 28-56 | 700–5600 | 92.50% | 7.68” | 2.6” | 1.44”
 |  |  |  |  | WHSG-1M1UNV210P-200L | 200W | 75-150 | 500–2100 | 93.40% | 7.68” | 2.6” | 1.44”
 |  |  |  |  | WHSG-1M1UNV110P-200L | 200W | 143-286 | 350–1100 | 93.60% | 7.68” | 2.6” | 1.44”
 |  |  |  |  | WHSG-1M1UNV670P-240L | 240W | 28-56 | 700–6700 | 92.80% | 7.68” | 2.6” | 1.44”
 |  |  |  |  | WHSG-1M1UNV210P-240L | 240W | 90-180 | 500–2100 | 93.60% | 7.68” | 2.6” | 1.44”
 |  |  |  |  | WHSG-1M1UNV110P-240L | 240W | 171-342 | 350–1100 | 93.80% | 7.68” | 2.6” | 1.44”
 |  |  |  |  | WHSG-1M1UNV760P-320L | 320W | 30-60 | 1500–7600 | 93.40% | 9.57” | 2.99” | 1.63”
 |  |  |  |  | WHSG-1M1UNV210P-320L | 320W | 120-240 | 500–2100 | 94.20% | 9.57” | 2.99” | 1.63”
 |  |  |  |  | WHSG-1M1UNV110P-320L | 320W | 229-457 | 350–1100 | 94.30% | 9.57” | 2.99” | 1.63”
IP66
100%-10%
WHCC-1M1UNV210P-75L | 75W | Line-Neutral 6kV, 120-277VAC Line & Neutral- 28-56VDC | 350-2100mA | 100%-10% cULus L
 |  | Ground 10kV |  | 
T1M1UNV240P-96L* | 96W | Line-Neutral 4kV, 120-277VAC Line & Neutral- 30-56VDC | 700-2400mA | 100%-10% cULus L Class
 |  | Ground 6kV |  | 
WHCC-1M1UNV260P-100L | 96W | Line-Neutral 6kV, 120-277VAC Line & Neutral- 28-56DVC | 350–2670mA | 100%-10% cULus L Class
 |  | Ground 10kV |  | 
*RoHS Compliant |  |  |  | 
Application: Outdoor, Warehouse, Industrial
Universal Voltage Input: 120-277VAC
E ciency > 90% at Full load
Non-Class 2 Output
Programmable Output Current with Fulham’s SmartSet: TPSB-100
Dimmable: 0-10V from 100%-10%
Certification: cULus Listed (Class P), RoHS, IP66 rated, Dry, Damp, Type HL (IP67/Wet location option available)
Wire Type
EMI: FCC Part 15 Class B
Input Surge Protection: Line-Neutral 6KV, Line & Neutral-Ground 10KV
Aluminum Extrusion heatsink housing
IP66 Dimmable Constant Current LED Driver
Coming Soon

## Slide 16
31
30
order@fulham..com
www..fulham..com
Universal Input: 120-277VAC
Class 2 output
  Programmable output current: 250mA-1500mA
  Output Voltage range: 10-57V
cULus listed, Class P
0-10V dimmable: 100%-1% or 0% (off )
Bluetooth Dimmable – Compatible with Fulham Smartlink
Linear form factor with wires
IP20 rating
Input Surge Protection: 2.5KV, common and differential mode
SmartSet and Handheld Programmer: TPSB-100
EliteBlue Driver (T2C1)
+1 323 599 5000
LED DRIVERS
PROGRAMMABLE LED DRIVERS
DRIVERS
DRIVERS
SugarCube Constant Current Drivers
Small or compact form factor LED drivers
Dedicated or Universal Voltage input
Class 2
Multiple Dimming types offered
Dedicated or Programmable Current
Part Number | Max Output Power | Input Voltage | Output Voltage Range (VDC) | Programable Output Current Range (mA) | Dimming Type & Range | Typical Efficiency at Max Load | Certification | Dimensions (inches) L W H | IP Rating
T1T11200350-15L | 15W | 120VAC | 20~42VDC | 350mA | TRIAC/ELV, 100%-10% | 82% | cURus | 3.94” | 1.18” | 0.91” | IP64
TC11200350-15C* | 15W | 120VAC | 24~50VDC | 350mA | N/A | >80% | cURus | 2.57” | 1.77” | 0.98” | Damp
T1M1UNV0350-15L*** | 15W | 120-277VAC | 18~45VDC | 350mA | 0-10V, 100%-10% | 85% | cULus Listed, Class P | 3.94” | 1.18” | 0.9” | IP64
T1T11200700-30L | 30W | 120VAC | 21~42VDC | 700mA | TRIAC/ELV, 100%-10% | 82% | cURus | 4.65” | 1.18” | 1.16” | IP64
T1T11200700-30C | 30W | 120VAC | 21~42VDC | 700mA | TRIAC/ELV, 100%-10% | 82% | cURus | 3.35” | 2.56” | 0.75” | IP64
T1M1UNV0700-30L*** | 30W | 120-277VAC | 18-45VDC | 700mA | 0-10V, 100%-10% | 86% | cULus Listed, Class P | 4.65” | 1.18” | 1.16” | IP64
SCCC-2U1UNV180P-65C** | 65W | 120-277AC 10-54VDC |  | 300-1800mA 0-10V/ELV/TRIAC;5%- 86% cULus Listed, Class P 4.98” 2.37" 1.05" IP20 100%, 0% |  |  |  |  |  |  | 
*Planned Phase-Out **Coming Soon ***RoHS Compliant
Dont see it? Ask for it!
Part Number | Max Input Output Voltage Power | Output Voltage Range (VDC) | Programable Output Current Range (mA) | 0-10V Dimming Range | Typical Efficiency at Max Load | AUX Output | Dimensions (inches)
 |  |  |  |  |  |  | L W H
T2C1UNV150P-40L
40W 120-277VAC 10~57VDC
250-1500mA
100-1%, Dim to off
89%
N/A
6.61”
1.97”
1.18”
Factors considered when deciding whether to use Constant Current or Constant Voltage include how the system will be installed, how it will be configured, and overall system e ciency requirements.
With Constant Current, the LED driver feeds a steady current through all LEDs on the module. Since each individual LED requires a certain voltage for the current to flow (known as Vf), the driver must provide enough voltage to equal the sum total of all the voltages of that module’s LEDs. Note that, while the LED module is frequently designed with all LEDs connected in one continuous serial electrical chain, it is also possible to create branches that split the current flowing through the module. So it’s essential to understand the design of the module’s circuitry, and
the electrical rating of the LEDs themselves when connecting a Constant Current driver to Constant Current LED modules. Constant Current architectures offer higher operating e ciency than Constant Voltage, but
less flexibility in connecting different modules and LEDs to the driver.
With Constant Voltage, the LED driver provides a steady voltage supply that enables power to flow through all LEDs connected. Since any given current flow requires a specific amount of voltage for each individual LED, it is necessary to buffer or regulate the voltage with a resistor (or equivalent component) in line with the connected LEDs. With proper resistance selection, the series connected LEDs receive proper -- never excessive -- voltage to regulate the current inflow. The Constant Voltage approach is most commonly used when the number of LED modules varies widely from different installations or product designs.
DID YOU
KNOW?
There are 2 different approaches to the electrical interconnection between LED driver and modules: Constant Current and Constant Voltage
Fulham’s revered product quality and world-class customer responsiveness make us the preferred partner to over 3000 lighting manufacturers and distributors worldwide.
Fulham’s rigorous quality control program ranks among the highest in the industry. Come to us with your application details and requirements. We can get back to you with the feasibility of a Custom solution!
ENGINEERED FOR DURABILITY
Large highest commercial grade electrolytic capacitors on the output side, specified for 10,000 hours at 105 degrees. Within the driver we have a self- regulating temperature design ensuring our confident 5 year warranty.
ENGINEERED FOR PERFORMANCE
The Lumo Series’ low ripple design creates a very stable power output for flicker-free lighting and smooth dimming. Making your LED lighting perform to the higest possible standards.
ENGINEERED FOR SIMPLICITY
A wide voltage range that can power a wide variation of LED fixtures. Taking out the complexity of your Supply chain.
ENGINEERED FOR EFFICIENCY
Active flyback leakage energy recovery circuit bringing the driver efficiency
up to 92% or higher, minimizing temperature increase.
ENGINEERED FOR PERFORMANCE
Low ripple design creates very stable power output for flicker-free lighting and smooth dimming. Making your LED lighting perform to the highest possible standards.
ENGINEERED FOR RELIABILITY
An active surge suppressor protects the driver from disturbances on the mains.

## Slide 17
33
32
order@fulham.com
+1 323 599 5000
www.fulham.com
12VDC or 24VDC Output
0-10V Dimming; 100% -10%
Linear form factor
Dimmable Constant Voltage LED Drivers
12VDC or 24VDC Output
Linear form factor
Non-Dimmable Constant Voltage LED Drivers
Dimmable Constant Voltage LED Drivers |  |  |  |  |  |  | 
Model Number | Output Output Output Watts Current Voltage (W) (mA) (VDC) | Input Voltage (VAC) | Ch. | Surge Protection L-N L&N-G | IP | Dimensions (L x W x H) | Case Type
T1M1UNV012V-20L† | 20 | 1660 | 12 | 100-277; 50/60Hz | 1 | 1kV | 2kV | 62 | 6.30” x 1.57” x 0.98” | Linear w/End Leads
T1M1UNV024V-20L | 20 | 833 | 24 | 100-277; 50/60Hz | 1 | 1kV | 2kV | 64 | 6.30” x 1.57” x 0.98” | Linear w/End Leads
T1M1UNV012V-60L† | 60 | 5000 | 12 | 100-277; 50/60Hz | 1 | 2kV | 4kV | 64 | 9.49” x 1.69” x 1.22” | Linear w/End Leads
T1M1UNV024V-60L* | 60 | 2500 | 24 | 100-277; 50/60Hz | 1 | 2kV | 4kV | 64 | 9.49” x 1.69” x 1.22” | Linear w/End Leads
T1M1UNV012V-75L† | 75 | 6250 | 12 | 100-277; 50/60Hz | 1 | 2kV | 4kV | 64 | 9.49” x 1.69” x 1.22” | Linear w/End Leads
T1M1UNV024V-75L | 75 | 3125 | 24 | 100-277; 50/60Hz | 1 | 2kV | 4kV | 64 | 9.49” x 1.69” x 1.22” | Linear w/End Leads
Non-Dimmable Constant Voltage LED Drivers
Model Number
Input Voltage (VAC)
Surge Protection
Ch. IP
Dimensions (L x W x H)
Case Type
L-N L&N-G
Output Output Output Watts Current Voltage
(W) (mA) (VDC)
20 833 24
60 5000 12
60 2500 24
60 5000 12
60 2500 24
75 6250 12
75 3125 24
T1UNV024V-20L*
100-277; 50/60Hz
1
1kV 2kV 62
2kV 4kV 64
2kV 4kV 66
2kV 4kV 68
2kV 4kV 64
2kV 4kV 64
2kV 4kV 64
2kV 4kV 64
6.30” x 1.57” x 0.98”
Linear w/End Leads
T1UNV012V-60LF †
100-277; 50/60Hz
1
9.49” x 1.69” x 1.22”
Linear w/End Leads
T1UNV024V-60L
100-277; 50/60Hz
1
9.49” x 1.70” x 1.21”
Linear w/End Leads
T1UNV012V-60LG*
100-277; 50/60Hz
1
9.53” x 1.67” x 1.34”
Linear w/End Leads
T1UNV024V-60LF
100-277; 50/60Hz
1
9.49” x 1.69” x 1.22”
Linear w/End Leads
T1UNV012V-75L* †
100-277; 50/60Hz
1
9.49” x 1.69” x 1.22”
Linear w/End Leads
T1UNV024V-75L* †
100-277; 50/60Hz
1
9.49” x 1.69” x 1.22”
Linear w/End Leads
THCV1UNV024V-100L** 100 4100 24
* Made to Order
**This driver is cULus Listed.
†Pending phase out; check with your Fulham rep for availability.
120-277; 50/60Hz
1
10.47” x 1.69” x 0.96”
Linear w/End Leads
Exporting to Europe? Fulham Lumo Series is your answer.
Fulham Lumo Series drivers are built on core engineering
design principles for exceptional standards of performance and reliability in LED systems. Highest grade critical components together with design features
for thermal management ensure excellent reliability. Low ripple designs create flicker-free lighting and perfectly smooth dimming.
Simplicity of specification and installation is a key characteristic of all Fulham Lumo Series drivers, hence the wide voltage and current ranges and industry leading low inrush current.
Ask your Fulham representative for more details about the Fulham Lumo Series.
fulham.com/product-systems/led-systems/lumoseries/
Surge protection, overload protection
Low temperature performance
Ideal for signage, cove, and niche applications
Surge protection, overload protection
Low temperature performance
CONSTANT VOLTAGE LED DRIVERS
CONSTANT VOLTAGE LED DRIVERS
DRIVERS
DRIVERS
* Made to Order
†Pending phase out; check with your Fulham rep for availability.

## Slide 18
34
order@fulham.com +1 323 599 5000 www.fulham.com 35
35
34
LED Modules & LED Retroﬁt Kits
If you have not reviewed Fulham’s LED Module and Retrofit Kit offerings and capabilities lately, you may be surprised at the breadth and depth of the product lines. This is another focus area for Fulham that contains both general use items, as well as ESSENTIAL specialty ones for applications such as Germicidal UV and Horticulture luminaires. As you page through, pay particular attention to our cuttable modules and outdoor ones for wall packs, canopies and more. The development of custom modules is another area in
which Fulham shines. We’re capable of quick turn samples and rapid development for the right opportunities. Ask us how!

## Slide 19
37
36
order@fulham.com
+1 323 599 5000
www.fulham.com
board linking
3 SDCM for high color consistency
CRI90 Standard, meets CEC Title 24 requirement
Range of common lengths and wattages to fit a variety of luminaires
Model Number VMU045005EC9xxA | Number of LEDs 12 | Nominal Input Current* (mA) 350 | Forward Voltage (VDC) 11.5 | Nominal Power (W) 4.0 | Dimensions (L x W) (including connector) 1.5” x 0.94” x 0.22” | Lumens @4000K/80CRI (lm) 554 | Nom. Efficacy @4000K / 80 CRI (lm/W) 138
VMU045005EC9xxB | 12 | 350 | 11.5 | 4.0 |  | 605 | 150
* Max input current 450mA. See specification sheets for detailed informa
Beam Angle | 120º
Operating Temperature Range | -35°C to +45°C (-31°F to 113°F)
Lumen Maintenance | L70 = 60,000hrs @ Tc=105ºC / L90 = 40,000hrs @ Tc=105ºC
Color Consistency | Binning per ANSI C78.377-2008; 4 SDCM
PCB Material | FR-4
Warranty | 5 years @ Max Tc from the date of manufacture
Safety/compliance | cURus (File # E351548), Class 2 Lighting System, RoHS Compliant
High e cacy: up to 150 lm/W @ 350mA, 4000K/90 CRI
On board connectors allow easy wire connections and end-to-end
450mA ECO Series DC LED Modules
Specifications
Operating Temp. Range
-40°C to 55°C / -40°F to 131°F
PCB Material
Color Consistency
Binning per ANSI C78.377-2015 @ 25°C; 3 SDCM
Warranty
Lumen Maintenance
L70: >60,000Hrs / L90: 40,000Hrs (meets DLC Premium and Standard requirements)
Safety/compliance
Product Models |  |  |  |  |  |  |  | 
Model Number / Dimension | Number | Input Current | Nom.Fwd. | Nom. Rated | Max. Fwd. | Max. Rated | Nom. Lum. | Nom. Efficacy
(L x W x H) | of LEDs | (mA) | Voltage (VDC) | Power (W) | Voltage (V) | Power (W) | @4000K/80CRI (lm) | @4000K/80CRI (lm/W)
VMU048012LPyxxA |  | 175 | 22.3 | 3.9 | 25 | 4 | 799 | 205
5.51” x 1.26” x 0.29” | 24 | 350 | 23.1 | 8.1 | 25 | 9 | 1518 | 187
(140mm x 32mm x 7.4mm) |  | 480* | 23.8 | 11.40 | 26 | 12 | 1959 | 172
VMU064025LPyxxA |  | 350 | 34.0 | 11.9 | 37 | 13 | 2347 | 197
 |  | 450 | 34.7 | 15.6 | 38 | 17 | 2942 | 189
10.94” x 1.26” x 0.29” | 48 |  |  |  |  |  |  | 
(278mm x 32mm x 7.4mm) |  |  |  |  |  |  |  | 
 |  | 640* | 35.6 | 22.8 | 39 | 25 | 3919 | 172
VMU045010EC9xxA | 24 | 350 | 23.0 | 8.1 | 5” x 0.71” x 0.22” | 1096 | 136 |  |  |  |  |  |  |  | 
VMU045010EC9xxB | 24 | 350 | 23.0 | 8.1 | 11” x 0.71” x 0.22” | 1172 | 145 |  |  |  |  |  |  |  | 
VMU045010EC9xxC | 24 | 350 | 23.0 | 8.1 | 17” x 0.71” x 0.22” | 1172 | 145 | VMU080030LPyxxA | 350 | 33.7 | 11.8 | 37 | 13 | 2380 | 202
 |  | 22.01” x 1.26” x 0.29” | 60 | 700 | 35.1 | 24.6 | 39 | 27 | 4418 | 180
tion on input current levels. |  | (559mm x 32mm x 7.4mm) |  | 800* | 35.6 | 28.5 | 39 | 31 | 4899 | 172
VMU125050LPyxxA |  | 350 | 32.9 | 11.5 | 35 | 12 | 2425 | 211
 |  | 700 | 34.1 | 23.9 | 36 | 26 | 4698 | 197
22.01” x 1.26” x 0.29” | 96 |  |  |  |  |  |  | 
(559mm x 32mm x 7.4mm) |  |  |  |  |  |  |  | 
 |  | 1250* | 35.5 | 44.4 | 38 | 49 | 7700 | 173
VMU140055LPyxxB† |  | 700 | 33.8 | 23.7 | 36 | 25 | 4736 | 200
33.07” x 1.26” x 0.29” | 108 | 1050 | 34.7 | 36.4 | 38 | 39 | 6847 | 188
(840mm x 32mm x 7.4mm) |  | 1400* | 35.5 | 49.7 | 39 | 55 | 8656 | 174
VMU140055LPyxxA |  | 700 | 33.8 | 23.7 | 36 | 25 | 4736 | 200
 |  | 1050 | 34.7 | 36.4 | 38 | 39 | 6847 | 188
44.13” x 1.26” x 0.29” | 108 |  |  |  |  |  |  | 
(1121mm x 32mm x 7.4mm) |  |  |  |  |  |  |  | 
 |  | 1400* | 35.5 | 49.7 | 39 | 55 | 8656 | 174
VMU140055LPyxxC† |  | 700 | 33.8 | 23.7 | 36 | 25 | 4736 | 200
45.98” x 1.26” x 0.29” | 108 | 1050 | 34.7 | 36.4 | 38 | 39 | 6847 | 188
(1168mm x 32mm x 7.4mm) |  | 1400* | 35.5 | 49.7 | 39 | 55 | 8656 | 174
VMU240095LPyxxA |  | 700 | 33.0 | 23.1 | 35 | 24 | 4838 | 209
 |  | 1400 | 34.2 | 47.9 | 37 | 52 | 9331 | 195
44.13” x 1.26” x 0.29” | 180 |  |  |  |  |  |  | 
(1121mm x 32mm x 7.4mm) |  |  |  |  |  |  |  | 
 |  | 2400* | 35.6 | 85.4 | 39 | 94 | 14,699 | 172
VMU240095LPyxxC† |  | 700 | 33.0 | 23.1 | 35 | 24 | 4838 | 209
57.95” x 1.26” x 0.29” | 180 | 1400 | 34.2 | 47.9 | 37 | 52 | 9331 | 195
(1472mm x 32mm x 7.4mm) |  | 2400* | 35.6 | 85.4 | 39 | 94 | 14,699 | 172
* Indicates maximum rated current. Modules may be operated at a current less than or equal to this value, below the Tc rating.
† Made to order. Minimum order quantity applies.
Part Numbering Key
30 A
Standard: 8 = 80
Made-to-order: 9 = 90
Color Temperature
Standard:
30 = 3000K
35 = 3500K
40 = 4000K
50 = 5000K
27 = 2700K
57 = 5700K
65 = 6500K
Made-to-order:
MCPCB (Aluminium Clad)
5 years @ 105ºC Tc from the date of manufacture
cURus (File # E351548), UL Class 2 Lighting System, CE, SELV, RoHS Compliant
Low Proﬁle Linear High Output DC
LED Modules
Ideal replacement for T5HO in linear highbays, water/vapor proof, and recessed and wall luminaires
Aluminium extrusion mount provides superior thermal management
Low profile design for use in smaller luminaires
Constant current, high-e cacy LEDs, 3 SDCM for high color consistency
Up to 219 lm/W; output range 234 lm to 14,699 lm (@4000K/80CRI)
Optional lenses snap on in seconds (See page 25)
LED MODULES
LED MODULES
MODULES
MODULES
Cover up to 16,000 lumens per single module
Up to 175lm/W at maximum input power
Typical 3 SDCM for high color consistency
Ideal for DLC Standard and Premium
Long lifetime: L70 > 60,000hrs; L90 = 40,000hrs
Warranty: 5 years
VIZION Cuttable LED Modules
Next generation flexible designs for high output linear applications. 46” length cuttable at the center. Push-in connectors for easy wiring. Standard mounting hole patterns for compatibility with existing luminaires.
Model Number
LED | Lumens @ | Max Input | Input | Forward
Qty | 4000K/80CRI | Current | Power | Voltage
Efficacy
L (")
W (")
H (")
Master Carton Qty
Standard Stock
VMU096030CT8xxA-46 | 60 | 4,338 | 960mA | 28.4W | 29.5VDC | 153lm/W | 46 | 0.72 | 0.22 | 100 | MTO V M U 240 095 LP 8 | 
VMU096045CT8xxB-46 | 90 | 7,452 | 960mA | 42.6W | 44.4VDC | 175lm/W | 46 | 0.72 | 0.22 | 100 | MTO | 
VMU160070CT8xxA-46 | 144 | 10,122 | 1600mA | 66.2W | 41.4VDC | 153lm/W | 46 | 0.72 | 0.22 | 100 | MTO | 
VMU260095CT8xxA-46 | 192 | 16,126 | 2600mA | 92.4W | 35.6VDC | 175lm/W | 46 | 0.72 | 0.22 | 100 | MTO | CRI
VMU252095CT8xxCT-48 144 | 14,385 | 2520mA | 91.6W | 36.4VDC | 157lm/W | 48 | 0.75 | 0.17 | 100 | MTO

## Slide 20
39
38
order@fulham.com
+1 323 599 5000
www.fulham.com
(mA)
Product Models |  |  |  |  |  | 
Model Number / Number Input Dimension (L x W x H) of LEDs Current | Nom.Fwd. Voltage (VDC) | Nom. Rated Power (W) | Max. Fwd. Voltage (V) | Max. Rated Power (W) | Nom. Lum. @4000K/80CRI (lm) | Nom. Efficacy @4000K/80CRI (lm/W)
TMU125050CLyxxA 350 | 33 | 12 | 35 | 12 | 2245 | 195
22” x 1.73” x 0.39” 96 1050 | 35 | 37 | 38 | 40 | 6210 | 169
(560mm x 44mm x 10mm) 1250* | 36 | 44 | 39 | 49 | 7130 | 161
TMU140055CLyxxA |  | 350 | 33 | 11 | 34 | 12 | 2255 | 196
44.1” x 1.73” x 0.39” |  |  |  |  |  |  |  | 
(1120mm x 44mm x 10mm) | 108 |  |  |  |  |  |  | 
 |  | 1050 35 36 38 39 6340 174 |  |  |  |  |  | 
TMU140055CLyxxB† |  |  |  |  |  |  |  | 
33.7” x 1.73” x 0.39” (840mm x 44mm x 10mm) |  | 1400* 36 50 39 55 8015 161 |  |  |  |  |  | 
TMU240095CLyxxA
44.1” x 1.73” x 0.39”
(1120mm x 44mm x 10mm)
350 32 11 34 12 2230 198
180
TMU240095CLyxxC†
58” x 1.73” x 0.52”
1400 34 48 37 52 8640 180
2400* 36 85 39 94 13610 159
naires
Accessories for Low Profile Linear HO & Linear HO Output DC Modules |  |  | 
Model Number | Description | Model Number | Description
TLE-OPT-120-002 | 5.5” snap-on lens, 82% transmissivity | TLE-OPT-120-021* | 58” snap-on lens, 82% transmissivity
TLE-OPT-120-003 | 11” snap-on lens, 82% transmissivity | TLE-OPT-120-020 | Standard LinearHO module end caps (2 pieces)
TLE-OPT-120-004 | 22” snap-on lens, 82% transmissivity | VLE-OPT-120-012* | Low Profile LinearHO module end caps (2 pieces)
VLE-OPT-120-033D* | 33” snap-on lens, 82% transmissivity | TLC-HN02 | 22” wire harness for 1 or 2 modules in parallel
TLE-OPT-120-013 | 44” snap-on lens, 82% transmissivity | TLC-HN04 | 22” wire harness for 3 or 4 modules in parallel
TLE-OPT-120-014* | 46” snap-on lens, 82% transmissivity |  | 
Specifications |  |  | 
Operating Temp. Range | -40°C to 55°C / -40°F to 131°F | PCB Material | CEM3
Color Consistency | Binning per ANSI C78.377-2015 @ 25°C; 3 SDCM | Warranty | 5 years @ 105ºC Tc from the date of manufacture
Lumen Maintenance | L70: >60,000Hrs / L90: 40,000Hrs (meets DLC Premium and Standard requirements) | Safety/compliance | cURus (File # E351548), UL Class 2 Lighting System, CE, SELV, RoHS Compliant
T M U 240 095 CL 8 30 A
CRI
(1473.2mm x 44mm x 13.3mm) | VR44-MU-295-840-1050A | 44” | 2 | 1 | 120-277 | 0.337 | 0.153 | 40.2 | 85 | 6756 | 168
* Indicates maximum rated current. Modules may be operated at a current less than or equal to this value, below the Tc rating. | VR44-MU-295-840-1400A |  | 2 | 1 | 120-277 | 0.445 | 0.202 | 52.5 | 88 | 8960 | 171
† Made to order. Minimum order quantity applies. | VR44-MU-495-840-2400A |  | 4 | 1 | 120-277 | 0.746 | 0.339 | 87.1 | 90 | 15,404 | 177
Part Numbering Key | Values reflect performance at 277VAC unless otherwise specified. |  |  |  |  |  |  |  |  |  | 
Color Temperature |  |  |  |  |  |  |  |  |  |  | 
Standard: 8 = 80
Made-to-order: 9 = 90
Standard:
30 = 3000K
35 = 3500K
40 = 4000K
50 = 5000K
27 = 2700K
57 = 5700K
65 = 6500K
Made-to-order:
Ideal replacement for T5HO in linear highbays, water/vapor proof, and recessed and wall lumi aires
Aluminum extrusion mount for thermal management with positioning magnets
LED at each end and connector underneath for even light distribution
Constant current, high-e cacy LEDs, 3 SDCM for high color consistency
Up to 198 lm/W; output range 2,200 lm to 13,310 lm (@4000K/80CRI)
Linear High Output DC LED Modules
Universal voltage (120V-277V) with high power factor and low THD
Multiple color temperatures: 3000K, 3500K, 4000K, 5000K
Modules feature aluminum extrusion heatsink with positioning magnets
UL Classified for field installation: 5-10 minutes per kit installation
Optimized for use with Fulham HotSpot LED Emergency backup systems
0-10V dimmable
5-year warranty
Listed on DLC Qualified Product List for utility rebate eligibility. Visit www.fulham.com/utilityrebates to learn more.
Product Models
Model Number
Length LED
Modules
Number of Number of
LED
Drivers
Input Voltage (VDC)
Total System Power (W)
Driver Efficacy (%)
Input Current (A)
120V 277V
0.117 0.053
0.114 0.052
0.241 0.109
0.347 0.157
0.242 0.110
0.237 0.107
Total Total
System System
Lumens Efficiency
(lm) (lm/W)
2245 164
2266 170
4490 166
6634 160
4480 165
4460 168
VR22-MU-150-840-0350A
22”
1
1
120-277
13.7
84
VR22-MU-250-840-0350A
2
1
120-277
13.3
84
VR22-MU-250-840-0700A
2
1
120-277
27.1
85
VR22-MU-250-840-1050A
2
1
120-277
41.4
85
VR44-MU-195-840-0700A
1
1
120-277
27.2
85
VR44-MU-295-840-0700A
2
1
120-277
26.6
85
Luminous Flux De-Rating: CCT and CRI Multipliers |  |  |  |  |  |  | 
 | 2700K | 3000K | 3500K | 4000K | 5000K | 5700K | 6500K
CRI 80 | 0.92 | 0.95 | 0.97 | 1.00 | 1.01 | 1.01 | 1.00
Complete LED retrofit kit: modules, driver, wiring harness, installation hardware, and UL labels
Linear High Output LED
Retroﬁt Kits
DID YOU
KNOW?
The correlated color temperature (CCT) of white light is expressed in degrees Kelvin (K)
Degrees Kelvin is a temperature measurement as commonly understood. But in the context of “color temperature” it can be misleading, since that expression refers to the spectral quality of the color emitted by a light source -- not its hotness, chill or color saturation.
That quality of light, described in Kelvin (K), ranges from yellowish “soft white” at the low end (standard household bulbs); through “bright white” (big retail store lighting); to “daylight” at the upper (bluish- white) end. The lower the “K” (2700 - 3000) the “warmer” the light quality; the higher the “K” the “cooler” as it rises to the blue end of the spectrum (5000+K).
Fulham offers several different popular color temperatures to meet customer requirements.
*Made to order.
LED MODULES
LED MODULES & RETROFIT KITS
MODULES
MODULES

## Slide 21
41
40
order@fulham.com
+1 323 599 5000
www.fulham.com
Outdoor Street, Wallpack and Canopy Modules
Highbay and Lowbay LED Modules
13” diameter round constant current DC modules
Suitable for high output low bay and high bay applications
3 SDCM for high color consistency
Options for dual-channel 200W max. and single-channel 100W max.
Each channel for use in UL Class2 lighting system
High e cacy up to 200lm/W; output range 3,000 lm to 32,000lm
Suitable for 30W – 200W per single module
Each input channel for use in UL Class 2 applications
High lumen output, high e cacy
Compatible with a wide range of 3rd party lenses
Typical 3 SDCM for high color consistency
Ideal for DLC Standard and Premium
Warranty: 5 years
Specifications |  |  | 
Operating Temp. Range | -40°C to 55°C / -40°F to 131°F | PCB Material | MCPCB (Aluminium Clad)
Color Consistency | Binning per ANSI C78.377-2015 @ 25°C; 3 SDCM | Warranty | 5 years @ 105ºC Tc from the date of manufacture
Lumen Maintenance | L70: >60,000Hrs / L90: 40,000Hrs (meets DLC Premium and Standard requirements) | Safety/compliance | cURus (File # E351548), UL Class 2 Lighting System, RoHS Compliant
Product Models
Model Number
Number Number of Wiring of LEDs Input Channels Diagram
Input Current* (mA)
Forward Voltage
Nominal Lumens Nom. Efficacy Power @4000K/80CRI @4000K / 80 CRI
(lm/W)
VMU240095HB8xxA** | 208 | 1 | #1
VMU240095HB8xxB** | 312 | 1 | #1
VM2240190HB8xxA**
416
2
#2
 | (VDC) | (W) | (lm) | 
1200 | 36.4 | 43.7 | 8085 | 185
2400 | 38.2 | 98.7 | 14701 | 160
1200 | 35.8 | 42.9 | 8416 | 196
2400 | 37.0 | 88.9 | 16074 | 181
1200 | 35.4 | 42.4 | 8320 | 196
2400 36.5 87.4 16170 185
#3
1200 x 2 36.4 87.4 16170 185
2400 x 2 | 38.2 | 183.4 | 29401 | 160
1200 | 34.9 | 41.8 | 8549 | 204
2400 1200 x 2 | 35.8 35.8 | 85.8 85.8 | 16833 16833 | 196 196
2400 x 2 | 37.0 | 177.8 | 32149 | 181
#2
#3
* Max input current 2400mA. See specification sheets for detailed information on input current levels.
** Made to Order across seven CCT options (2700, 3000, 3500, 4000, 5000, 5700 and 6500K). The xx in each part number denotes CCT through use of the first two digits of each, e.g. 27 = 2700K. Limited stock of 80CRI 3000K & 5000K is available.
VM2150170LN8xxA-16 | 240 | 25,410 | 1500mA*2 | 164.8W | 54.9VDC | 154lm/W | 16.20 | 0.92 | 0.06 | 100 | MTO |  |  |  | 
VMU140050LN8xxA-12 | 108 | 8,030 | 1400mA | 49.8W | 35.6VDC | 161lm/W | 12.20 | 0.92 | 0.06 | 100 | MTO |  | VMU2240190HB8xxB** | 624 | 2
VMU240090LN8xxA-12 | 180 | 13,721 | 2400mA | 85.7W | 35.7VDC | 160lm/W | 12.20 | 0.92 | 0.06 | 100 | MTO |  |  |  | 
Outdoor Street Modules |  |  |  |  |  |  |  |  |  | 
Model Number | LED Qty | Lumens @ 4000K/80CRI | Max Input Input Power Current | Forward Voltage | Efficacy (lm/W) | L (") | W (") | H (") | Master Carton Qty | Standard Stock
VMU200100HS7xxA 16
11,129
2000mA
100W
50VDC
111
2.76
2.76
0.24
100
MTO
VMU140052RT7xxA 12
8,638
1400mA
51.8W
37VDC
167
5.71
1.71
0.24
100
MTO
Wiring Diagram #1
Wiring Diagram #2
Wiring Diagram #3
LED Driver2 2.4A, 100W
LED Driver1 2.4A, 100W
Line
Neutral
LED Driver 2.4A, 100W
Line
Neutral
LED Driver 2.4A, 100W
Line
Neutral
LED MODULES
LED MODULES
MODULES
MODULES
Fulham’s versatile outdoor series modules are ideal for street lights, wallpacks and canopy applications. Each module comes with push-in connectors for easy wiring, and standard mounting hole patterns for compatibility with 3rd party lenses and standard luminaires.
Outdoor Wallpack Modules
Model Number
LED Lumens @ Qty
4000K/80CRI Current
Max Input Input Power
Forward Voltage
Efficacy
L (")
W (")
H (")
Master Carton Qty
Standard Stock
Outdoor Canopy Modules |  |  |  |  |  |  |  |  |  | 
Model Number | LED Qty | Lumens @ 4000K/80CRI | Max Input Input Power Current | Forward Voltage | Efficacy | L (") | W (") | H (") | Master Carton Qty | Standard Stock
VM2240100RT8TWA
(Tunable White)
420
18,021
2400mA
95.4W
39.8VDC
189lm/W
11
4
0.29
20
MTO
VM2240200RT8xxA 420
34,901
2400mA*2
198.6W
41.4VDC
176lm/W
11
4
0.29
20
MTO
VMU240100RT8xxA
210
17,450
2400mA
99.3W
41.4VDC
176lm/W
11
4
0.29
20
MTO

## Slide 22
43
42
order@fulham.com
+1 323 599 5000
www.fulham.com
Very low flicker, meets Title 24 requirements
DirectAC Drive with integrated LED board
Smooth TRIAC/ELV dimming down to 10%
Kits include installation hardware and labels
ens -
es
Specifications
Input Voltage | UNV (120-277VAC) 50/60 Hz
Beam Angle | 120º
Estimated Lumen Maintenance (L70) | Circular and Rectangular models: L70 > 54,000hrs / L90 = 20,000hrs Linear models: L90 = 35,000hrs
Flicker Percentage | <30%
Operating Ambient Temp. Range (Ta) | -35ºC to +50°C
PCB Material / Lens Material | MCPCB (superior thermal management) / Optical Grade Polycarbonate (5VA Flame rated)
Safety/Compliance | cULus Classified (File# E486779), cURus (File# E486778), RoHS Compliant, ENERGY STAR® Luminaire 2.0 Listed and CSD, JA8 Compliant (2700-4000K @90CRI)
Protections | Surge 2.5V Common and Differential mode; Over Temperature Protection
Warranty | 5 Years @ specified Tc from the date of manufacture
Product Models
Model Number
CRI
Available CCT
Shape
ENERGY STAR
Listed*
ENERGY STAR CSD*
TJTUNV010AC9xxB
Input Power
10W
Max Lumens @4000K**
1065
90
Standard options: 2700K, 3000K,
3500K, 4000K
Made-to-order:
VJTUNV010LN9xxB05
10W
1087
90
VJTUNV015LN9xxB11
15W
1644
90
TJTUNV015AC9xxB
15W
1680
90
TJTUNV015AR9xxB
15W
1725
90
Circular
Linear
Linear Circular Rectangular
Dimensions (Inches)
3.11 Dia. x 0.71 H
5.52 L x 2.21 W x 0.67 H
11.03 L x 2.21 W x 0.67 H
5.08 Dia. x 0.75 H
7.40 L x 4.00 W x 0.71 H
TJTUNV023AC9xxB | 23W | 2540 | 90 | 5000K | Circular | 6.97 Dia. x 0.71 H
VJTUNV030LN9xxB22 | 30W | 3235 | 90 |  | Linear | 22.06 L x 2.21 W x 0.67 H
TJTUNV034AC9xxB | 34W | 3685 | 90 |  | Circular | 9.55 Dia. x 0.81 H
* ENERGY STAR designations: Listed = Luminaire 2.0. CSD= Certified Subcomponent Database
High voltage barrier and 5VA flame rated lens -
suitable for open or fully enclosed luminaires
JA8 Compliant
DirectAC LED Retroﬁt Kits
Part Numbering Key
V J T UNV 030 LN 9 30 B 22
Shape
AC = Circular LN = Linear
AR = Rectangular
Color Temperature Standard:
27 = 2700K
30 = 3000K
35 = 3500K
40 = 4000K
Made-to-order:
50 = 5000K
CRI
9 = 90
Dedicated 120V input AC Engine
CCT Selectable: 2700K, 3000K, 3500K, 4000K, 5000K (Two Power-
Selectable Models, as well)
CRI90 standard, meet CEC Title 24 requirement
Potassium Fluorosilicate (PFS) phosphor LEDs to achieve as high
e cacy as today’s CRI80 LEDsSimple installation can be done in the field in minutes
Suitable for open or fully enclosed luminaires
Suitable for luminaires with plastic and glass lenses
cULus Classified 1598C as complete kit
Uses cURus Recognized 8750 individual components
Compatible with Fulham Emergency Driver FHSCP-UNV-6W-L-SD and Fulham 25W Micro-Inverter FHUPS1-UNV-25L-SD
ENERGY STAR® Luminaire 2.2 Listed and CSD
VividHorse 120VAC AC Engine Retroﬁt Kits - CCT Selectable & Power Selectable
Product Models
(inches)
Model Number Max Input Power(W) Lumens @4000K Standard CRI Shape Dimensions |  |  |  |  |  | ENERGY STAR Listed* | ENERGY STAR CSD*
VJT120010AC9TWB | 10 | 980 | 90 | Circular | 3.11 Dia x 0.71 H |  | 
VJT120010LN9TWB-06 | 10 | 980 | 90 | Linear | 6.2 L x 2.41 W x 0.67 H |  | 
VJT120020AC9TWB | 15 or 20 (power selectable) | 1500 or 2000 | 90 | Circular | 5.12 Dia x 0.65 H |  | 
VJT120030AC9TWB | 25 or 30 (power selectable) | 2500 or 3000 | 90 | Circular | 6.64 Dia x 0.65 H |  | 
5000K
OFF ON
4000K
OFF ON
3500K
OFF ON
3000K
OFF ON
2700K
OFF ON
Power Selector on two higher-powered Round models
CCT Switch common to all
models
15 or 20
25 or 30
LED RETROFIT KITS
LED RETROFIT KITS
MODULES
MODULES

## Slide 23
45
44
order@fulham.com
+1 323 599 5000
www.fulham.com
Suitable for 2’x2’ and 2’x4’ luminaires
Universal Voltage with 0-10V dimming
Meets CEC Title 24 JA10
3 selectable power levels per Model
Offers opportunities for SKU reduction
Optional Occupancy Sensor (ELMOPLX00SR)
LED Troffer retrofit kits completely assembled within frame DLC Listed
Roomside Installable
CCT Selectable (3500K-5000K)
UL 1598C, suitable for dry or damp locations
12VDC AUX output
Compatible with Fulham Emergency Driver FHSCP-UNV-4W-L
VividHorse LED Troffer Retroﬁt
Product Models
Model Number | Input Power(W) | Lumens @4000K | Standard CRI | Dimensions (inches)
VTR-22-MU-30-9TW-A | 20 / 25 / 30 | 2640 / 3225 / 3,780 | 90 | 23.8 L x 23.8 W x 3.09 H
VTR-24-MU-45-9TW-A | 34 / 38 / 45 | 4488 / 4902 / 5,670 | 90 | 47.8 L x 23.8 W x 3.09 H
Suitable for 2’x2’ and 2’x4’ luminaires
Universal Voltage with 0-10V dimming
Meets CEC Title 24 JA10
3 selectable power levels per Model
Offers opportunities for SKU reduction
LED Panel retrofit kits completely assembled within frame DLC Listed
Roomside Installable
CCT Selectable (3500K-5000K)
UL 1598C, suitable for dry or damp locations
12VDC AUX output
Compatible with Fulham Emergency Driver FHSCP-UNV-4W-L
VividHorse LED Panel Retroﬁt
Product Models |  |  |  | 
Model Number | Input Power(W) | Lumens @4000K | Standard CRI | Dimensions (inches)
VPR-22-MU-25-9TW-A | 18 / 22 / 25 | 2376 / 2838 / 3150 | 90 | 23.8 L x 23.8 W x 2.2 H
VPR-24-MU-36-9TW-A | 23 / 30 / 36 | 3036 / 3870 / 4536 | 90 | 47.8 L x 23.8 W x 2.2 H
Specifications
Input Voltage | 120~277VAC +/- 10% (50/60Hz)
Operating Temperature Range | -35°C to 60°C / -31°F to 140ºF
Lumen Maintenance @105ºC | L70= >60,000 hours / L90= 36,000 hours (@Tc max = 96ºC)
Dimming Type / Range | 0-10V / 100% ~ 10%
Color Consistency | Binning per ANSI C78.377-2015 @25°C; 3 SDCM
PCB Material / Connector Qty / Em. Connection | CEM1 / 2 / Yes
Input Surge Test | 2.5kV Common and Differential mode (Per ES Ring Wave Test)
Warranty | 5 years @ Max. Tc from the date of manufacture
Safety/compliance | cURus (File # E351548, E342838), cULus (File # E365124), RoHS Compliant, Energy Star Luminaire 2.2 Listed and CSD
Dual channel LEDs, Dip Switch on PCB for six-level-CCT selectable: 2700K, 3000K, 3500K, 4000K, 4500K and 5000K
CRI90 standard; advanced phospor technology LEDs for superior CRI90 e cacy
Protects investment by preserving existing luminaires
No bulbs to change means lower maintenance costs
Simple installation can be done in the field in minutes
ENERGY STAR® Luminaire 2.2 Listed and CSD for utility rebate eligibility. Visit www.fulham.com/utilityrebates to learn more.
Kits include installation hardware, required UL Classified labels, and installation instructions
Product Models |  |  |  |  |  |  | 
Model Number | Number of LEDs | Input Nom. Lum. Power @4000K/ (W) 90CRI (lm) | Engine Efficacy @90CRI (lm/W) | Shape | Dimensions (inches) | ENERGY STAR Listed* | ENERGY STAR CSD*
VKMUNV008RD930A | 48+48 | 10 | 1400 | 140 | Round | 7.83 Dia. x 0.92 H
VKMUNV008RT930A | 48+48 | 10 | 1400 | 140 | Rectangular | 7.4 L x 4.7 W x 0.92 H
VKMUNV012RD930A | 72+72 | 14.5 | 2160 | 148 | Round | 7.83 Dia. x 0.92 H
VKMUNV018RD930A | 48+48 | 21 | 2650 | 126 | Round | 7.83 Dia. x 0.92 H
VKMUNV018RT930A | 48+48 | 21 | 2650 | 126 | Rectangular | 7.4 L x 4.7 W x 1.18 H
VKMUNV025RD930A | 72+72 | 29.5 | 3730 | 126 | Round | 7.83 Dia. x 1.18 H
* ENERGY STAR designations: Listed = Luminaire 2.2. CSD= Certified Subcomponent Database, 4500K is not certified by ENERGY STAR
VividHorse DC LED Engine
Retroﬁt Kits - CCT Selectable
Part Numbering Key
V K M UNV
Default CCT setting is 3000K.
Pre-setting to other CCTs is made to order. Contact Fulham for details
A
Color Temperature
27 = 2700K 40 = 4000K
30 = 3000K 45= 4500K
35 = 3500K 50 = 5000K
025 RD 9 30
RD = Round
RT = Rectangular
CCT Selection Dip Switch
Modules Only (2022 Series) |  |  |  | 
Model Number | Nominal Input Power @ Max. Input Current | Shape | Max Input Current | Nom. Lum. Flux @5000K/90 CRI
VMU095023RD9TWA | 23W | Round | 950mA | 3,463lm
VMU095034RD9TWA | 34.5W | Round | 950mA | 5,194lm
VMU095023RT9TWA | 23W | Rectangular | 950mA | 3,463lm
LED RETROFIT KITS
LED RETROFIT KITS
MODULES
MODULES

## Slide 24
47
46
order@fulham.com
+1 323 599 5000
www.fulham.com
Horticultural Modules
Product Models
Made to Order
VHU150080LNFWRB-46
VHU150080LNFWRC-46
Come to us with your specific application details and requirements. We’ll get back to you with the feasibility of producing a custom solution!
?
Dont see it? Ask for it!
A distinct advantage of Fulham is that we are the actual design engineers. Fulham is not merely a buyer / multiple-lister /
re-brander and reseller.
White & Red Spectrum for Horticulture Applications
Suitable for Multi-layer Cultivation of Leafy Vegetables
PPF/W up to 3.0 umol/j at Hot State
46” in length
SPECIALTY LED MODULES
SPECIALTY LED MODULES
MODULES
MODULES
UVC LED Products
Ideal UVA light source for curing, Photo-catalyst and detecting applications
Near-UV (UVA) and visible light range, harmless to human body or eyes
Available in 365nm and 395nm peak wavelength options
Available in rigid 11” & 22” strips
For use in UL Class 2 lighting systems
High e ciency germicidal UVC radiation, 270nm peak wavelength
395nm UVA + 270nm UVC in-one LED package, visual indicator when UVC is on
8”L x 1.26” W rigid strip with aluminum extrusion, superior thermal management
24VDC constant voltage input, for use in UL Class 2 lighting systems
11” Compatible with LEDiL VIOLET 12X1 UVC lens
Specifications |  |  | 
Operating Temp. Range | -20°C to 55°C / -4°F to 131°F | Max. Tc temperature | 80°C / 176°F
Warranty | 5 years @ 80ºC Tc from the date of manufacture | Safety/compliance | cURus (File # E351548), UL Class 2 Lighting System, RoHS Compliant
Specifications |  |  | 
Operating Temp. Range | -20°C to 45°C / -4°F to 113°F | Max. Tc temperature | 50°C / 122°F
Warranty | 3 years @ 50ºC Tc from the date of manufacture | Safety/compliance | cURus (File # E351548), UL Class 2 Lighting System, RoHS Compliant
Product Models |  |  |  |  |  |  |  | 
Model Number | Number of LEDs | Dimension (L x W x H) | Type | Peak Wavelength (nm) | Input Current* (mA) | Forward Voltage (VDC) | Nominal Power (W) | Radiation Power (W)
VUU064025LP365A† | 10.94” x 1.26” x 0.29” Constant | 365 - 370 | 640* | 38.8 | 24.8 | 0.60
VUU064025LP395A† | 48 (278 x 32 x 7.4mm) Current | 395 - 400 | 640* | 38.8 | 24.8 | 8.97
VUU125050LP365A† | 22.01” x 1.26” x 0.29” Constant | 365 - 370 | 1250* | 38.9 | 48.6 | 1.17
VUU125050LP395A† | 96 (559 x 32 x 7.4mm) Current | 395 - 400 | 1250* | 38.9 | 48.6 | 17.53
† Made to Order
Product Models |  |  |  |  |  |  |  | 
Model Number | Number of LEDs | Dimension (L x W x H) | Type | Peak Wavelength (nm) | Input Current* (mA) | Input Voltage (VDC) | Nominal Power (W) | UVC Radiation Power (mW)
VUU24V005LP270
C -8* 9 8” x 1.26” x 0.29” (203 x 32 x 7.4mm) | Constant Voltage | UVC: 270 - 280 UVA: 395 - 405
11” x 0.756” x 0.27” | Constant | UVC: 270 - 280
C -11* 12 (281 x 19.2 x 6.8mm) | Voltage | UVA: 395 - 405
145 | 24.0 | 4.5 | 45
270 | 24.0 | 6.5 | 60
VUU24V007LN270
* Made to Order
UVA LED Products

## Slide 25
order@fulham.com +1 323 599 5000 www.fulham.com 49
4848
49
48
Fluorescent Ballasts
Fulham’s fluorescent programs are the bread and butter upon which its reputation was established more than a quarter century ago. The products were so well engineered that many remain as relevant today as when introduced and are known industry-wide as the reliable “workhorses” that inspired their first branding. Jump to today, and Fulham has expanded to include ESSENTIAL Refrigeration ballasts and Programmable Germicidal UV Ballasts, as well as Remote Mount, CFL, and small form factor varieties for numerous field replacement and factory install scenarios.

## Slide 26
51
Note: To order a specific factory set current other than the default set current add -XXXX after part number where XXXX is replace with the output current desired. For example if 500mA is required you would add -0500 after the part number to order this model. This would be a made to order model. Additional validation testing will be required and updates to any safety certifcations will be required for any lamp combination not already listed with the ballast.
* Made to order. Minimum order quanities will apply. †Open Frame PCBA. No enclosure and no potting. §Flying leads connection type ** 100%,75%,50% *** 100%-50%
50
order@fulham.com
+1 323 599 5000
www.fulham.com
Specifications |  | 
Input Voltage | 120V-277V; 50/60Hz | 
High Power Factor | > 0.98 | 
ATHD | < 10% | 
Lamp Operation Mode | Programmed Start | 
Ignition Method | Programmed Pre-Heat Start | 
Min. Operating Temperature | -30°C (-22°F) | 
Case Qty. (pcs.) | 25 | 
Low Temperature Ballasts
that automatically adjust in cold temperatures to provide optimal light output.
12.03” x 1.71” x 1”
Fluorescent Low Temperature Electronic Ballasts Lamp Operation Model Number Max. Current (A) Max. Power (W) Dimensions (L x W x H) Weight (lbs) Case Qty. (pcs.) # of Lamps Lamp Type / Designation |  |  |  |  |  |  | 
IH1-UNV-232-T8 | .85 | 100 |  | 1.4 | 25 | 1 or 2 | F25 / F32 / F40 T8
IH2-UNV-270-T8 | 1.35 | 155 |  | 1.5 | 25 | 1 or 2 | F58 / F70 T8
IH3-UNV-272T12HO
1.38
150
1.4 25
1 or 2
F48 / F60 T8HO, F48 / F60 T10VHO, F48 / F60
/ F72 T12HO
1 F72T8HO, F72T10VHO, F96T12VHO
UV Germicidal & Tanning Ballasts
for air and water purification purposes
Standard Molex®
Connectors
for Plug-n-Play commercial refrigeration applications
Molex is a registered trademark of Molex Incorporated.
“
B
e
S
u
r
e
I
t
’
s
P
u
r
e
”
Programmable Sunhorse Ballasts
for Germicidal UV applications and Tanning
Specifications | SHS15P-UNV-H | SHS4P-UNV-C
Output Current Range (+/-10%) | 800-1050mA @310W 1060-1200mA @260W 800mA default | 340-840mA 800mA default
Input Voltage | 120-277V (UNV) | 112W: 120-277V (UNV) 95W: 100V
Frequency Rating | 50/60Hz | 50/60Hz
Max Ballast Wattage | 310W/260W | 112/95W
Power Factor | >0.9 | >0.9@≥60W load
Total Harmonic Distortion | See spec sheet | ≤20%@≥60W load
Start Type | Programmed Rapid Start Type R.S | Programmed Rapid Start Type R.S
L x W x H (in) | 10.00 x 2.80 x 1.79 | 6.77 x 3.02 x 1.27
L x W x H (mm) | 254 x 71.1 x 45.4 | 172 x 76.7 x 32.2
Minimum Starting Temperature | -20ºC (-4ºF) | -20ºC (-4ºF)
CULUS and CE | Yes | Yes
PSE (for Japan) | - Yes | 
Legacy Fulham Programmer
TPSB-100 & New Display SHS-DISP
Multi-Ballast Monitoring/Control
Audible buzzer alarm notifications
Lamp failure and lamp hour end of life notifications
5VDC Digital Input for use with Smart and non-smart ballasts
Can operate as a standalone lamp hour counter for non-smart ballastsballasts
Powered by SHS Ballast RJ12 connection (directly from the ballast), 24VDC Barrel Plug, 12VAC/24VAC, or USB-C
The new SunHorse Digital LCD Display SHS-DISP is a more robust device that expands user options. Attributes include:
Remote ON/OFF Port Connection turns Output ON/OFF w/o removing input power to ballast
NO/NC Relay
Lamp Status 5VDC Digital Output
Future I2C Sensor Implementation
SHS15P-UNV-H & SHS-DISP
combination spec sheet
SHS4P-UNV-C & SHS-DISP
combination spec sheet
TPSB-100 spec sheet
SHS-DISP
TPSB-100
Operating Max. Input Factory Set Default Min. Max. Model Number Voltage Current (A) Output Current Output # of Max. Total Lamp Certification Dimming Operating Case Dimensions (VAC) Range (mA) Current Lamps Load Type Temp. Temp. (L x W x H) (mA) |  |  |  |  |  |  |  |  | 
Non-Dimming |  |  |  |  |  |  |  |  | 
SHS1-UNV-C* | 120-277 | 0.55A | 170-425 | 425 | 1 or 2 | 55W | - -30°C | 75°C | 5.06" x 2.36" x 0.988"
SHS1-UNV-C-I | 120-277 | 0.40A | - | 400 | 1 or 2 | 45W | - -30°C | 75°C | 5.06" x 2.36" x 0.988"
SHS1-UNV-C-0170* | 100-277 | 0.29A | - | 170 | 1 or 2 | 28.2W | - -30°C | 90°C | 5.06” x 2.36” x 0.988”
SHS2-MLT-L* | 120-240 | 0.33A | - | 400 | 1 | 41W | - 0°C | 75°C | 6.45" x 1.49" x 0.96"
SHS3-MLT-L* | 120-240 | 0.29A | - | 800 | 1 | 58W | - 0°C | 75°C | 6.45" x 1.49" x 0.96"
SHS5-024-C | 24 | 2.59A | - | 400 | 1 or 2 | 41W | - 0°C | 75°C | 3.64" x 3.12" x 1.01"
SHS10-UNV-H* | 120-277 | 1.4A | 800-1000 | 1000 | 1 | 190W | - -20°C | 70°C | 10" x 2.55" x 1.26"
SHS11-UNV-H | 120-277 | 1.4A | 680-1000 | 800 | 1 or 2 | 200W | - -20°C | 70°C | 10" x 2.55" x 1.26"
SHS14-UNV-H | 120-277 | 1.282A | 400-600 | 425 | 1 or 2 | 160W | - -20°C | 70°C | 10" x 2.55" x 1.26"
SHS15-UNV-H* | 120-277 | 2.7A | 800-1200 | 800 | 1 or 2 | 310W@<1050mA 260W@>1050mA | - -20°C | 83°C | 10" x 2.8" x 1.79"
SHGS1-MID-2-200-L*§ | 200-277 | 2.1A | 1400-2200 | 1600 | 1 or 2 | 400W | - 0°C | 70°C | 12" x 3.11" x 1.73"
SHGS1-MID-2-200-N*†§ | 200-277 | 2.1A | 1400-2200 | 1600 | 1 or 2 | 400W | - 0°C | 70°C | 9.84" x 3.49" x 1.55"
SHGS1-MID-2-200-N-C*† | 200-277 | 2.1A | 1400-2200 | 1600 | 1 or 2 | 400W | - 0°C | 70°C | 9.84" x 3.49" x 1.55"
FEP-120-600-L
120
2.86A
-
wire
600 - 800 per 1, 2, 3 or 4
320W
-
-18°C
70°C
19.25" x 3" x 1.25"
FEP-230-600-L
230
1.50A
-
wire
600 - 800 per 2, 3 or 4
320W
-
0°C
70°C
19.25" x 3" x 1.25"
Dimmable |  |  |  |  |  |  |  |  |  |  | Displays stored data about lamp manufacturer and part number
SHGA1-MID-2-200-N*†§ | 200-277 | 2.1A | 1400-2200 | 1600 | 1 or 2 | 400W | DALI** | 0°C | 70°C | 9.84" x 3.49" x 1.55" | from SunHorse ballast memory
SHGA1-MID-2-200-N-C*† | 200-277 | 2.1A | 1400-2200 | 1600 | 1 or 2 | 400W | DALI** | 0°C | 70°C | 9.84" x 3.49" x 1.55" | 
SHGA1-MID-2-200-L* | 200-277 | 2.1A | 1400-2200 | 1600 | 1 or 2 | 400W | DALI** | 0°C | 70°C | 9.84" x 3.49" x 1.55" | 
SHD21-230-L-I | 230 | 1.64A | - | 2100 | 1 | 320W | 0-10V*** | 0°C | 70°C | 16.69" x 1.72" x 1.18" | 
FLUORESCENT BALLASTS
FLUORESCENT BALLASTS
FLUORESCENT
FLUORESCENT

## Slide 27
53
52
order@fulham.com
+1 323 599 5000
www.fulham.com
Specifications | 
Power Factor | >0.9
THD | <34.6%
EMI/RFI Compliance | FCC Part 18-A
Sound Rating | “A”
Ballast Type | Instant Start
Voltage Transients | ANSI C82.11 - 1993
Input / Protection | FUSE
Remote Mounting | 20ft Max
Min. Operating Temp | -30°C (-20°F)
Max. Case Temp | 70°C (158°F)
Approvals / Class | cULus Listed, Class “P”, 1 or 2 Outdoor
Dedicated Voltage (120, 230, and 277V) |  |  |  |  |  | 
Series | Model Number | Input Max Voltage (V) Power (W) | Max Current (Amp) | Dimensions (L x W x H) | Configuration | Case Qty.
WORKHORSE 2
35
WH2-120-C
120
.33
3.36” x 1.84” x 1.01”
Compact case, side leads
50
WORKHORSE 22
35
 | WH2-277-L | 277 |  | .15 | 5.52” x 1.25” x 0.99” | Linear case, side leads | 50
 | WH2-277-C | 277 |  | .15 | 3.37” x 2.32” x 1” | Compact case, side leads | 50
WH22-120-L 120 .25 |  |  |  |  | 5.52” x 1.25” x 1.02” | Linear case, side leads | 50
WH22-120-C
120
.25
3.36” x 1.84” x 1.01”
Compact case, side leads
50
WORKHORSE 3
WH3-120-L
120
64
.56
6.48” x 1.50” x 1.02”
Linear case, side leads
50
WH3-120-C
120
.56
3.8” x 2.5” x 1.01”
Compact case, side leads
60
WH3-230-L*
230
.29
6.45” x 1.5” x 1”
Linear case, side leads
50
WH3-277-L
277
.24
6.48” x 1.5” x 1.02”
Linear case, side leads
50
WH3-277-C
277
.24
3.83” x 3.11” x 1.01”
Compact case, side leads
60
WORKHORSE 33
WH33-120-L
120
64
 | WH33-120-C | 120 |  | .53 | 3.64” x 3.12” x 1.01” | Compact case, side leads | 60
WORKHORSE 4 | WH4-120-L | 120 | 70 | .56 | 6.48” x 1.5” x 1.02” | Linear case, side leads | 50
 | WH5-120-L | 120 |  | 1.15 | 8.5” x 1.73” x 1.01” | Linear case, side leads | 50
WORKHORSE 5 | WH5-230-L | 230 | 128 | 0.57 | 9.5” x 1.73” x 1.01” | Linear case, side leads | 50
 | WH5-277-L | 277 |  | 0.48 | 9.5” x 1.73” x 1.01” | Linear case, side leads | 50
.53
6.48” x 1.5” x 1.02”
Linear case, side leads
50
WORKHORSE 6
WH6-120-L
120
140
 | WH6-277-L | 277 |  | 0.50 | 9.5” x 1.73” x 1.01” | Linear case, side leads | 50
 | WH7-120-L | 120 |  | 1.82 | 19.24” x 1.72” x 1.03” | Linear case, side leads | 25
WORKHORSE 7 | WH7-120-H | 120 | 220 | 1.82 | 11.73” x 3.23” x 1.23” | H can w/ magnetic footprint | 16
 | WH7-230-L | 230 |  | 1.10 | 19.24” x 1.72” x 1.03” | Linear case, side leads | 25
 | WH8-120-L | 120 |  | 1.8 |  |  | 
WORKHORSE 8 220 19.24” x 1.72” x 1.03” |  |  |  |  |  | Linear case, side leads | 25
1.04
8.5” x 1.73” x 1.01”
Linear case, side leads
50
WH8-230-L*
230
0.79
Universal Voltage (120-277V)
Model Number Dimensions (L x W x H) Input Current Master Carton Qty.
WH41-UNV-L* 9.48” x 1.41” x 1.02” 0.496A 25
Fluorescent Ballasts
Specifier Grade T8 Specifications
Power Factor
98.5% Min.
ATHD
Less than 10%
EMI
FCC CFR Title 47 Part 18 non-consumer
Ballast Factor
>.87
Starting Method
Instant Start
Regulatory Approvals
UL & cULus Listed Type 1 or Type 2
Inherent Thermal Protection
Class P
Transient Protection
C62.41 Class A 7 strikes
Dimensions (L x W x H)
WHSG2: 9.50” x 1.38” x 0.99”
WHSG3: 9.53” x 1.32” x 1.05”
WORKHORSE 1 | WH1-120-L | 120 | 28 | .10 | 5.92” x 0.94” x .76” | Linear case, side leads | 90 |  | WHSG4: 9.53” x 1.32” x 1.05”
 | WH2-120-L | 120 |  | .33 | 5.52” x 1.25” x 1.02” | Linear case, side leads | 50 | Lamp CF | < 1.7
Min. Starting Temp.
0°F (-18°C)
Weight
1.5 lbs. (700g)
Specifier Grade T8 Ballasts
Model Number
Input Voltage (VAC)
Input Power (W)
Max. Current (A)
Black/White Wires
Red Wires
Blue Wires
Yellow Wires
Case Qty (pcs.)
WHSG2-UNV-T8-IS
120-277; 50/60Hz
59
.50
25”
46”
31”
N/A
25
WHSG3-UNV-T8-IS
120-277; 50/60Hz
85
.71
25”
46”
31”
N/A
25
WHSG4-UNV-T8-IS
120-277; 50/60Hz
112
.93
25”
46”
31”
46”
25
Fluorescent Speciﬁer Grade
Ballasts
Remote Mount Electronic Ballasts
WH43-UNV-L 9.48” x 1.41” x 1.02” 0.88A 25
WH44-UNV-L 9.48” x 1.41” x 1.02” 0.496A 25
*Made to order.
•
•
•
•
•
•
Operates up to 20ft. from lamp Versatile
High Power Factor Energy Saving Lightweight
Solid-State Electronics
Fluorescent Low Temperature Electronic Ballasts
Model Number Lamp Watts / Type Lamps Operated Input Watts Line Current Ballast Factor Efficacy Factor
LH4-120L F28T5 2 55 0.48 1.0 1.7
Find WorkHorse and LongHorse wiring diagrams here: https:// www.fulham.com/contact-us/wiring-diagrams/
Or scan this QR Code with your SmartPhone’s camera >
*Made to order.
FLUORESCENT BALLASTS
FLUORESCENT BALLASTS
FLUORESCENT
FLUORESCENT

## Slide 28
55
54
order@fulham.com
+1 323 599 5000
www.fulham.com
SugarCube Electronic Ballasts
Model Model Number
Operates Lamps
Dimensions (Inches)
For T5 / T8 / T12
SC-120-108-LT5
1 x F4T5, F6T5, F8T5
H 4.76”, W 1.05”, L .76”
SC-120-213-LT5
1 x F21T5, F8T5 + F13T5; 2 x F13T5, F14T5, F15T8
H 5.53”, W 1.27”, L 1.01”
SC-120-115-CT8†
1 x F14T8, F15T8, F17T8, F14T12, F15T12, F20T12, CFQ13W
H 3.09”, W 1.45”, L 1”
SC-120-132-T8XL*
1 x F15T8, F17T8, F25T8, F32T8
H 6.3”, W 1.08”, L 1.01”
For CFL & Circle
SC-120-113-CFL
1 x 13CFQ/E, F15T8, F17T8, 13W Spiral
H 3.09”, W 1.45” L 1”
For UV Lamps
SC-120-287-CUV
1 x 180mm T5 UV, 287mm T5 UV
H 3.07”, W 1.46”, L 1”
SC-230-287-CUV
1 x 180mm T5 UV, 287mm T5 UV
H 3.07”, W 1.46”, L 1”
For 230V
SC-230-113-CFL*
1 x 13CFQ/E, 13FTR/E
H 3.09”, W 1.45”, L 1”
Pony Electronic Ballasts
SugarCube Ballasts
Pony Electronic Ballasts
Model Model Number Operates Lamps Dimensions (Inches)
Pony for CFL
NPY-120-118-CFL* 1 x 13CFT/E, 18CFQ/E, 18CFTR/E H 1.03”, W 1.76”, L 3.36” NPY-120-126-CFL 1 x 18CFT/E, 24/27CFT/E, 26CFQ/E, 26CFQ/E, 26CFTR/E, 32CFTR/E, 22CRT9 H 1.02”, W 2.39”, L 3.36”
NPY-120-218-CFL 2 x 13CFT/E, 18CFQ/E, 18CFTR/E H 1.02”, W 2.39”, L 3.36”
U.S INNOVATION BY
Fulham has a rich history of developing innovative, award-winning lighting solutions. From Fulham’s
U.S. Headquarters near Los Angeles, California, Fulham Product Managers, Engineers, Salespeople and Marketers team up to develop innovative, new product ideas that are then researched, designed and manufactured by Fulham’s own factories abroad. This all occurs under Fulham’s direct supervision as
a Prime Manufacturer, thus guaranteeing the extremely high quality upon which Fulham has built its reputation for over 25 years.
Our global lighting programs include:
Wireless Control Systems
Programmable LED Drivers
Standard LED Modules & Drivers
Horticulture Modules
Everyday Electronic Fluorescent Ballasts
Specialty Ballasts such as UV/Germicidal, Refrigeration, or Remote Mount
Emergency lighting
Custom solutions
And more...
Compact Fluorescent (CFL) Electronic Ballasts
T5HO & T5HE Fluorescent Ballasts
Model Number
Max. Load (W)
(A)
RHA-UNV-254-LT5
120W
1.0 A
9.53” x 1.32” x 1.05”
RHA-UNV-454-LT5†
240W
2.0 A
16.88” x 1.69” x 1.18”
Leads
† Made to order. Minimum order quantity applies.
Specifications
Operating Voltage | 120V-277V; 50/60Hz
ATHD | < 10%
Over Current | Fuse
Transient Protection | C62.41 Class A 7 strikes
Regulatory Approvals | UL & cULus Listed Type 1 Outdoor
EMI | FCC CFR Title 47 Part 18 non-consumer
High Power Factor | > .98
Ballast Maximum Case Temp. | 167ºF (75ºC) - 5 Year Warranty
Ballast Maximum Case Temp. | 194ºF (90ºC) - 3 Year Warranty
Lamp Starting Mode | Programmed Start
Inherent Thermal Protection | Class P
CFL Ballasts & Kits |  |  |  |  | 
Model Number | Max Load | Max. Current | Dimensions (L x W x H) | Weight | Case Quantity
RHA-UNV-226-C | 57W | .52 A 5.1” x 2.4” x 1” 5.2 oz. C Models: 50 pcs/ case (4.3” L case) Kits (K): 60 pcs/ case
RHA-UNV-242-C | 84W | .752 A 5.1” x 3” x 1.3” 7 oz. - (4.3” L case)
Max. Current
Dimensions (L x W x H)
Connector Type
Case Qty (pcs.)
Leads
25
20
T5HO & T5HE Fluorescent Electronic Ballasts
*Made to order.
* Made to Order
† These models are UL listed, not cULus.
FLUORESCENT BALLASTS
FLUORESCENT BALLASTS
FLUORESCENT
FLUORESCENT

## Slide 29
56
order@fulham.com +1 323 599 5000 www.fulham.com 57
Controllable Lighting Solutions
Wireless controllable lighting is an emerging area of focus and import for Fulham where our SIG Qualified Bluetooth® Mesh Lighting Control System attempts to marry convenience and function with lesser degrees of installation or usage complexity than are associated with other comparable systems. Fulham’s solution allows you to start
small in just one room, and then expand into larger areas, floors or an entire building as needs change. Our solution is supported by all the occupancy and daylighting sensors that you’d need to minimize energy usage and hasten ROI. Manage the system offsite via the EliteBlue web portal or on site from your SmartPhone.
57
56

## Slide 30
59
58
order@fulham.com
+1 323 599 5000
www.fulham.com
Fulham eliteBlue Commissioning Software
Fulham’s eliteBlue commissioning software provides an intuitive set of tools for commissioning and monitoring qualified Bluetooth mesh lighting devices. Using simple web and iOS apps, users can easily customize lighting control parameters in accordance with site-specific needs and building energy codes.
Bluetooth to 0-10V SmartBridge
A simple, easy-to-install component that connects to an existing 0-10V driver to add SIG Qualified Bluetooth mesh capability. The SmartBridge is an ideal solution for manufacturers looking to develop their Bluetooth product lines or contractors seeking to provide wireless lighting options in the field.
0-10V dimming standard. Add Bluetooth dimming with optional ESLI01HB01 SmartLink
Compatible with Fulham’s SmartSet programming platform
Specifications |  |  |  |  |  | 
Model Number | Input Voltage (VAC) | Watts | Output Voltage (VDC) | Dimensions (L x W x H) | Case Type | Case Qty.
T2C1UNV150P-40L | UNV (120-277) | 40 | 10-57 | 6.61" x 1.97" x 1.18" | Compact w/End Leads | 20
Bluetooth Accessories
Model Number
Description
ESLTOPJX00SR
Short-range PIR occupancy, daylight harvesting sensor and Bluetooth Radio for connected LED driver
ESLTOPJX00LR
Long-range PIR occupancy, daylight harvesting sensor and Bluetooth Radio for connected LED driver
ESLI01HB01
Bluetooth SmartLink (attaches to T2C1UNV150P-40L to provide Bluetooth capability)
ELIOPJX00SR
Short-range PIR occupancy and daylight harvesting sensor for SmartBridge
ELIOPJX00LR
Long-range PIR occupancy and daylight harvesting sensor for SmartBridge
ESRPB-W-EO
Single Rocker EnOcean Switch
EDRPB-W-EO
Double Rocker EnOcean Switch
CTGATBPOE*
IoT Bluetooth Gateway extends a mesh network with Internet access to visualize/analyze data
Specifications |  |  |  |  |  |  | 
Model Number | Max Load (W) | Max Input Current (A) | Input Voltage (VAC) | IP | Features | Dimensions (L x W x H) | Case Qty.
CTBRCB02JM02 | 600 | 5 | UNV (120-277) | 66 | On / Off, 0-10V Dimming Control, Sensor Input On / Off, 0-10V Dimming Control, Sensor Input, Color Control, Power Metering | 5.17" x 2.26" x 1.29" | 30
CTBRCB03JM03-PC* |  |  |  |  |  |  | 
Connected Driver
A 40W, 0-10V constant current driver with the unique ability to add Bluetooth mesh connectivity by attaching an intelligent Bluetooth antenna. Compatible with third-party sensors, wall switches, and other devices, the connected driver serves as the core component for powerful, easy-to- expand connected systems.
SIG Qualiﬁed Bluetooth® Mesh Lighting Control System
Bluetooth mesh is an emerging platform for connected lighting that is paving the way to IoT smart lighting. It provides fast, reliable performance, unmatched scalability, high-level security and out-of-the-box interoperability, creating opportunities for larger, more e cient lighting networks.
Wireless High speed communication at distances of over 300 feet, creating massive savings on installation and wiring
Scalable Start small with a single room, or connect thousands of devices in a building-wide installation
Secure Advanced encryption standards with multiple authentication keys for maximum protection
Reliable Self-healing network prevents communication losses and allows devices to be added or removed without disruption
Interoperable All SIG Qualified Bluetooth mesh devices can communicate seamlessly, regardless of manufacturer
Web portal
Used off site to manage lighting installation projects and plan commissioning, including mapping zones within a building, setting up control scenarios for zones and managing users collaborating on the project.
Try it at eliteblue.fulham.com
Mobile app for iOS
Used onsite to commission devices and fine-tune installations. No specialized training or lighting control expertise is needed- the intuitive interface lets you add Bluetooth mesh lighting devices to a wireless network in no time.
*Made to order.
WIRELESS CONTROL SYSTEMS
WIRELESS CONTROL SYSTEMS
CONTROLS
CONTROLS
* Made to Order

## Slide 31: WHY CHOOSE FULHAM?
61
60
order@fulham.com
+1 323 599 5000
www.fulham.com
LIMITED WARRANTY
Length of Warranty and Coverage
Warranty period will be determined from the date of manufacture as indicated by the date code stamped on each product and will be covered as follows:
EliteControl™ - 5 Years FireHorse™ - 5 Years HotSpot™ - 5 Years* IceHorse™ Ballast - 3 Years
LongHorse™ Electronic Remote Fluorescent Ballast - 5 Years LumoSeries™ - 5 Years
PONY™ Electronic Ballast - 2 Years PONY™ Electronic SugarCube™ - 2 Years PONY™ Electronic Transformer - 2 Years
RaceHorse™ Electronic Ballast – 70ºC 5 Years, 90ºC 3 Years
SunHorse™ Ballast - 3 Years SineHorse™ Ballast - 3 Years LED Drivers - 2 to 5 Years
VividHorse™ Retrofit Kits - 5 Years* Vizion™ Modules/Engines - 5 Years* Vizion™ Retrofit - 5 Years*
Vizion™ Luminaire - 5 Years*
WorkHorse™ Electronic Fluorescent Ballast - 5 Years
* Covered defects for Vizion, VividHorse, and HotSpot LED modules. For purposes of this limited warranty, a defect in a module shall be defined as one or more individual LEDs dark at initial installation or greater than 10% of individual LEDs dark during the Warranty Period. Replacement and/or repair of individual Vizion, VivdHorse, or HotSpot LED Modules does not extend this limited warranty beyond the original Warranty Period.
Warranty Conditions
Fulham extends this express limited warranty only to the original purchaser or to the first user. This constitutes the complete warranty for the product. Fulham is not responsible for any auxiliary equipment not furnished by Fulham, which is used in connection with or attached to the product, or for operation of the product with any auxiliary equipment. Damage to all such equipment is expressly excluded from this warranty. In addition, Fulham
is not responsible for any damage to the product resulting from the use of
auxiliary equipment not supplied by Fulham.
Warranty Conditions Not Covered
This warranty is not applicable to any product manufactured by Fulham not installed and operated in accordance with:
Underwriters Laboratories Inc. (UL)
National Electrical Code (NEC)
Standards set by the International Electrotechnical Commission (IEC)
European Norms Electrical Certification (ENEC)
Applicable international federal, state and local codes
Remote applications beyond maximum distance noted on product specification sheet. If maximum distance is not provided, remote application is not covered.
Fulham specific, most recent instructions and application guidelines
provided for installation of the product
Additionally, this warranty is not applicable to Fulham manufactured products that have been subjected to excessive stress including, but not limited to, operating temperatures exceeding the recommended maximum temperature on any part of the product.
Obtaining Warranty Service
If within the warranty period it appears that the installed product does not meet the warranty conditions specified, the purchaser must notify Fulham of its warranty claim. Fulham or its authorized service company will provide warranty service directly to you.
General Provisions
All responsibilities regarding the product are set forth by this warranty. Replacement or repairs of the product is your exclusive remedy. For purposes of clarity, “replacement or repairs of the product” does not include any removal or reinstallation costs or expenses, including, without limitation, any labor costs or expenses, shipping costs to return non-conforming products or any damages that may occur during the return of product
to Fulham. If Fulham chooses to replace the product and is not able to
do so because it has been discontinued or is not available, Fulham may replace it with a comparable product. Fulham reserves the right to use new, reconditioned, refurbished, repaired or remanufactured products or parts in the repair or replacement of any product covered by this warranty. If no
replacement product is available, Fulham, solely at its discretion, may issue a
credit for the product, prorated for its remaining warranty life.
This warranty is given in lieu of all other express warranties. Implied warranties, including those without limitation, warranties of merchant ability and fitness for a particular purpose, are limited to the duration of this limited warranty. Fulham shall in no event be liable for damages in excess of the purchase price of the product, for any loss of use, loss of time, inconvenience, commercial loss, lost profits or savings or other incidental, special or consequential damages arising out of the use or inability to use such product, to the full extent such may be claimed by law.
Local Exceptions
Some jurisdictions do not allow the exclusion or limitation of incidental or consequential damages, or limitations on how long an implied warranty lasts, therefore the above limitations or exclusions may not apply to you. This warranty gives you specific legal rights, and purchasers may have other rights that vary by jurisdiction.
Returned Materials Authorizations (RMA)
Customers shall contact Fulham directly for all RMA’s.
After receiving the RMA, the user shall promptly return the product at the user’s expense to Fulham after receiving instructions as to when and where to ship product. Failure to follow this procedure shall void this warranty.
Should the number of pieces received by Fulham differ from the RMA either
+/-, the customer will be notified and adjustments will be made at that time.
Fulham reserves the right to examine all failed products to determine the cause of failure and patterns of usage and reserves the right to be the sole judge as to whether any products are defective and covered under this warranty.
Contact Information
Fulham North America
+1 323 599 5001
warranty@fulham.com
Fulham Europe
+31 72 572 3000
warranty.eu@fulham.com
Effective: August 1st, 2018 Last Edit: June 16, 2023
Known and Trusted Worldwide:
Successful Global Operation
Stable:
Nearly 30 Year Legacy, Stand Behind Our Products
Reputation for Quality:
Minimal In-Field Service or Re-installations Required
Always Growing and Innovating:
We are the Engineers (Not Just Buyers and Resellers)
Relevant:
Strong foothold with new items in emerging markets; ongoing sales of legacy goods
Diversiﬁed in Technologies Served:
Powered Light, Emergency and Control all under one roof
Varied Solutions (General & Essential Specialty):
23 Year Germicidal UV Program, Programs
in Refrigeration, Horticulture and more
Resilient:
Diverse Customer Base
Differentiated:
Unique Sales and Marketing Approaches, broad product offering
not reliant on one technology
Leading:
#1 Independent Innovator of globally-mandated Emergency
Lighting Solutions
Insulated:
Redundant Sources of Supply (both India and Asia manufacturing)
FLUORESCENT BALLASTS
FLUORESCENT BALLASTS
Note: HotSpot™ EZExit products acquired after 12/31/23 are not warranted, serviced or supported by Fulham.

## Slide 32
www.fulham.com
India
Fulham Pvt. Ltd.
201, Kaliandas Udyog Bhavan Sadanand Tandel Marg Century Bazaar Lane Prabhadevi, Mumbai-400025 Tel: +91.22.66388775-8
sgaikwad@fulham.com
Fulham Pvt. Ltd. Survey No. 26-3 Village Narhe
Taluka Haveli, Dist: Pune - 411041
Tel: +91.20.24690703/4 Fax: +91.20.24690712
sgaikwad@fulham.com
Europe
Fulham Europe
sales.eu@fulham.com
China
Fulham Electronic Co. Ltd.
4th Floor, Building #18 8 Heying Road Changping District Beijing, P.R. China
Post Code: 102200
Tel: +86-10-6073-5858
order.china@fulham.com.cn
Hong Kong
Fulham Company Ltd. Unit 6, 6/F Kowloon Plaza 485 Castle Peak Road Cheung Sha Wan, Kowloon Hong Kong
Tel: +852.2314.4801
Fax: +852.2314.4186
hongkongsales@fulham.com
North America
U.S. Headquarters
12705 S. Van Ness Avenue Hawthorne, CA 90250
Order processing, technical support, product information, requests for quotations
Tel: +1 323.599.5000
Fax: +1 323.754.9060
order@fulham.com
Warranty Department
Tel: +1 323.599.5001
warranty@fulham.com
©2023 Fulham Co. Inc. All Rights Reserved.